Generic Hazard Analysis and
Critical Control Points

(HACCP)
Plan for the
Canadian Brewing Industry

A Project of
Brewers Association of Canada
HACCP Working Group

Revision Date:  November 2009
www.brewers.ca

Table of Contents

Introduction	5

HACCP Principle 1 - Hazard Identification	9

HACCP Principle 2 - Critical Control Points	10

HACCP Principle 3 - Critical Limits	11

HACCP Principle 4 - Establish Monitoring Procedures	11

HACCP Principle 5 - Establish Deviation Procedures	13

HACCP Principle 6 - Establish Verification Procedures	14

HACCP Principle 7 - Establish Record Keeping/Documentation	15

BAC Generic HACCP Program	17

Form 1:  Product/Process Description	19

Form 2:  List of Product Ingredients and Incoming Materials	23

Form 3:  Process Flow Diagram	27

Form 4:  Schematic Diagram	41

Form 5:  Hazard Identification Biological Hazards	45

Form 6:  Hazard Identification Chemical Hazards	57

Form 7:  Hazard Identification Physical Hazards	69

Form 8:  Critical Control Points	81

Form 3A:  Process Flow Diagram with CCPs	127

Form 5A:  Biological Hazards Control & CCPs	141

Table of Contents (Continued)

Form 6A:  Chemical Hazards Control & CCPs	153

Form 7A:  Physical Hazards Controls & CCPs	167

Form 9:  Hazards not Controlled by Brewery	181

Form 10:  HACCP Plan	185

HACCP Plan Appendices	193

Appendix 1- Form 3 - Information used for Flowcharts	195

Appendix 2- Form 8 – Critical Control Points	213

Appendix 3 - Form 10 - Additions for Low Alcohol Beer	217

Appendix 4 – Diagrams for Hazard Identification & CCP Decision Tree	221

Appendix 5 – BAC Glass Inclusion Reference	225

Appendix 6 – Blank Forms 1 - 10	229

Appendix 7 – Reference Literature	243

Introduction

HACCP (Hazard Analysis Critical Control Point) systems are required under proposed Health Canada’s Good Manufacturing Practices Regulations for Food.  Specifically, manufacturers must develop procedures to ensure products manufactured do not pose a health risk.

The HACCP program is a world-wide recognized systematic and preventative approach that addresses biological, chemical and physical hazards through anticipation and prevention, rather than by finished production inspection.

This document is a working guide to preparing a customized program of hazard analysis and identification of critical control points (CCP) for brewers, as an aid to consistent compliance and inspection by the Canadian Food Inspection Agency (CFIA).  This document is not a customized model per se.  Each brewer using this working guide is responsible for producing his or her own customized model.

Prior to the development and implementation of a HACCP program, establishments must have developed, documented and implemented programs to control factors that may not be directly related to manufacturing controls but support the HACCP plans and the Good Manufacturing Practices (GMP). These programs are called Pre-requisite programs.  These are discussed in detail in another document (see BAC- Generic Pre-requisite Programs).

There are 12 basic steps to implementing a HACCP program.  They are:

- Assemble the HACCP team;

- Describe the product;

- Identify intended uses;

- Construct process Flow Diagram and Plant Schematic;

- Verify on site the Flow Diagram and Plant Schematic;

Introduction (Continued)

- List hazards associated with each step  (Principle 1);

- Determine Critical Control Points (Principle 2);

- Establish Critical Limits (Principle 3);

- Establish Monitoring Procedures (Principle 4);

- Establish Deviation Procedures (Principle 5);

- Establish Verification Procedures (Principle 6); and

- Establish record keeping/documentation for Principles one through six (Principle 7).

This manual deals in detail with steps 1 through 8, which include Principles 1 through 3 of HACCP system elements.  It also discusses in general terms the follow-up requirements that make up steps 9 through 12.

Instructions for Companies

It is suggested that the user of this document becomes acquainted with the BAC – Food Safety Toolkit Introduction document before attempting to proceed with applying the recommendations herein.

There are also other BAC guidance documents that are to be used along with this BAC - Generic HACCP Plan model.  They are:

- BAC/HACCP Plan Workbook; and

- BAC/HACCP Plan Glossary.

Pre-requisite programs should be established before attempting to implement the HACCP program.

Each company will determine the appropriate internal procedures to follow to ensure that the programs are implemented as described and are effective.

Reminder - This document is not a customized model per se.  Each brewery using this working guide is responsible for producing its own customized HACCP program.

HACCP Working Group Members

The BAC HACCP Working Group was established under the direction of the Product Integrity Committee of the Brewers Association of Canada.

These Pre-requisite Programs have been developed by the Brewers Association of Canada (BAC) with a Technical Committee comprised of industry members, government representatives and food safety consultants.  The BAC acknowledges the committee members for their outstanding contribution to the BAC/HACCP project.

We also extend our appreciation and gratitude to Agriculture and Agri-Food Canada and the Canadian Food Inspection Agency for their financial and technical support of this project.

| Mr. B. Andrews | Molson Canada |
| --- | --- |
| Ms. E. Bounsall | Brasserie McAuslan |
| Ms. S. Buttenham | Sleeman Breweries Ltd. |
| Ms. M. Dewar | Brewers Association of Canada |
| Dr. T. Dowhanick | Labatt Breweries of Canada |
| Ms. A. Fuller | Great Western Brewing Company |
| Mr. L Harford | Brewers Association of Canada |
| Mr. M. Ligas | Magnotta Brewery |
| Mr. G. Muise | Pump House Brewery |
| Mr. R. Savage | Molson Canada |
| Mr. A. Kassianenko | Canadian Food Inspection Agency |
| Mr. G. Sundeen | Canadian Food Inspection Agency |
| Mr. F. Schreurs | Guelph Food Technology Centre |
| Mr. P. Medeirois | Guelph Food Technology Centre |
| Mr. K. McMillan | Guelph Food Technology Centre |
| Ms. A. Brown | Guelph Food Technology Centre |
| Ms. M. Harris-Bailey | Guelph Food Technology Centre |

HACCP Principle 1 - Hazard Identification

Principle 1: Conduct a hazard analysis.

- A product safety hazard is any biological, chemical, or physical property that may cause beer to be unsafe for human consumption.

- Breweries determine the product safety hazards and identify the preventive measures the plant can apply to control these hazards.

On the basis of available information for each of the ingredients used in beer and for each of the process steps in brewing, potential biological, physical and chemical hazards are identified.  Information sources include published databases, scientific literature, company records, external and internal audits etc.  In addition to identifying potential hazards, Forms 5, 6 and 7 are used to identify the control points.

Diagrams for Hazards Identification and CCP Decision Tree

Critical Control Points for breweries are determined using the HACCP Decision Tree.  The Decision Tree was first developed by a Codex Alimentarius working group on HACCP in June 1991. This Decision Tree has been slightly modified to include a prescreening question and preliminary instructions.

Pre-screening question = Determine if (hazard) fully controlled by Pre-requisite Programs.  If ‘yes’, indicate “Pre-requisite Program(s)” and proceed to the next identified hazard.  If ‘no’, proceed to Question 1. (See Appendix)

HACCP Principle 2 - Critical Control Points

Principle 2: Identify critical control points.

A critical control point (CCP) is a point, step, or procedure in a food process at which control can be applied and, as a result, a food safety hazard can be prevented, eliminated, or reduced to an acceptable level.

Using the Decision Tree, Form 8 is completed.  The last column is where Critical Control Points are identified.  CCP’s are labelled numerically with a category qualifier for Biological, Physical and Chemical (B, P or C) hazard and expected outcome of the control measure (elimination of risk(e), prevention (p), or minimize or reduce (r)).  In this model, the Critical Control Points in breweries were identified as follows:

| Step | CCP # |
| --- | --- |
| Empty Bottle Inspection | CCP1-P |
| Empty Bottle Inspection/ Residual Liquid Detector | CCP1-C |
| Filling (Auto-Flush Only) | CCP2-P |
| Internal Cleaning (Manual) | CCP3-C |

Hazards identified on Forms 5, 6 and 7 are either controlled at some point in the brewing process or cannot be controlled by the facility.  Form 9 is intended to identify control measures that do not take place in the brewery but are controlled elsewhere.  No such hazards were identified in the analysis of breweries.

HACCP Principle 3 - Critical Limits

Principle 3: Establish critical limits for each critical control point.

- A critical limit is the maximum or minimum value to which a physical, biological, or chemical hazard must be controlled at a critical control point to prevent, eliminate, or reduce to an acceptable level.

For each Critical Control Point, critical limits were established.  These are values which separate acceptability from unacceptability. They are intended to meet government regulations, industry standards or other scientific data.

# HACCP Principle 4 - Establish Monitoring Procedures

Principle 4: Establish critical control point monitoring requirements.

Monitoring is the act of conducting a planned sequence of observations or measurements of control parameters to assess whether a CCP is under control.

- Monitoring activities are necessary to ensure that the process is under control at each critical control point. Each monitoring procedure and its frequency will be listed in the HACCP plan.

At each CCP, the monitoring requirements and the means to ensure that the CCP remains within the critical limits are specified. Monitoring procedures generally relate to on-line processes and are usually by observation or by measurement.  The frequency of testing, who is responsible for carrying out the testing, and the testing procedures must also be specified. The monitoring specifications are written on Form 10 for each CCP.  Each brewery will develop its own specifications, where required.

Monitoring tracks the system's operation and allows for action to be taken in the event of a loss of control or where there is a trend toward the loss of control. It provides information to a brewery on a timely basis, allowing for decisions on the acceptability of the lot at a particular stage in the process. Monitoring procedures

# HACCP Principle 4 - Establish Monitoring Procedures (Continued)

performed in the establishment during operation will result in written documentation that will serve as an accurate record of the operating conditions.

If any of the critical limits is out of control as determined by the monitoring procedures, the CCP will be out of control. Lack of control at a CCP is defined as being a critical defect or a deviation. Deviations will result in the production of a hazardous or unsafe product Therefore, adequate and effective monitoring procedures are essential due to the serious consequences arising from deviations. Most monitoring procedures for CCPs must be rapid because they relate to on-line processes and there is not sufficient time for lengthy analytical testing. Physical and chemical measurements or visual observations are preferred because they can be done rapidly. All monitoring equipment must be properly calibrated for accuracy. Examples of some physical and chemical measurements taken to monitor the critical limits are: temperature, time and pH.

There are many ways to monitor critical control points. Monitoring can be done on a continuous or batch basis. The reliability of continuous monitoring (100 % is preferred where feasible). The established monitoring frequency must be sufficient to substantiate that the hazard is under control. Responsibility for monitoring is clearly identified and individuals monitoring the CCPs must be trained in the testing procedure and must fully understand the purpose and importance of monitoring. The individual must have ready access to the monitoring activity and must be unbiased in monitoring and reporting. Finally the individual must accurately report the monitoring activity.

All operational records and documents that are associated with CCP monitoring must be properly completed and signed by the person doing the monitoring and verified/signed by a responsible official of the company.

HACCP Principle 5 - Establish Deviation Procedures

Principle 5: Establish corrective actions.

- These are actions to be taken when monitoring indicates a deviation from an established critical limit. The final rule requires a plant's HACCP plan to identify the corrective actions to be taken if a critical limit is not met. Corrective actions are intended to ensure that no product injurious to health or otherwise adulterated as a result of the deviation enters commerce.

A deviation is defined as failure to meet the specified critical limits. Deviation procedures are pre-determined and document the set of corrective actions that are implemented when a deviation occurs.

All deviations must be corrected by taking appropriate corrective action(s) to control the non-compliant product and to correct the cause of non-compliance. The corrective action(s) taken must be recorded and filed.

A deviation procedure must describe the acceptable corrective action(s) for a deviation. The diversity of possible deviations at each CCP means that more than one corrective action may be necessary at each CCP. The corrective action(s) must correct the cause of the deviation and must control the actual or potential hazard resulting from the deviation. Product control includes proper identification, and handling of the affected lots. The deviation procedures at each CCP are written on Form 10.  These procedures will be developed by each brewery in accordance with the brewery’s requirements.

Corrective actions are prescribed and formalized so that employees responsible for critical control point monitoring understand and are able to perform the appropriate corrective action(s) in the event of a deviation.

HACCP Principle 5 - Establish Deviation Procedures (Continued)

When a deviation occurs, it will most likely be noticed during the routine monitoring of a CCP. A deviation results when the pre-determined critical limit for a CCP is out of compliance. If the proper corrective action is not taken the deviation may result in an unacceptable health risk.

# HACCP Principle 6 - Establish Verification Procedures

Principle 6: Establish procedures for verifying the HACCP system is working as 
                    intended.

- Validation ensures that the plans do what they were designed to do; that is, they are successful in ensuring the production of safe product. Plants will be required to validate their own HACCP plans.

- Verification ensures the HACCP plan is adequate, that is, working as intended. Verification procedures may include such activities as review of HACCP plans, CCP records, critical limits and  analytical data

Verification activities are methods, procedures and tests used to determine if the HACCP plans for that establishment are valid and are operating properly.

Verification activities are generally involved and may include analytical testing. In carrying out the verification activities, the establishment may find that some hazards were overlooked or they may discover new or unexpected hazards. In this case, the plan needs to be modified appropriately. The verification procedures at each CCP are written on Form 10 by each brewery in accordance with the brewery requirements. Both the establishment and the CFIA will have a role in verifying HACCP plan compliance and will carry out activities to verify that the HACCP plan is operating properly. Verification activities differ from monitoring activities. Results from verification activities are not intended to make decisions on the acceptability of lots of product. Verification activities involve for example, analytical testing or auditing of the monitoring procedures, product sampling, audits of monitoring and verification records.

# HACCP Principle 7 - Establish Record Keeping/ Documentation

Principle 7: Establish record keeping procedures.

- The HACCP program requires that all plants maintain certain documents, including its hazard analysis and written HACCP plan, and records documenting the monitoring of critical control points, critical limits, verification activities, and the handling of critical limit deviations.

The HACCP records are defined as the record keeping that is done at each CCP and that contain the information required to ensure that the HACCP plan is followed.

Records are essential in determining the compliance of the establishment in following the agreed-upon HACCP plan. The HACCP records differ from the records that are kept to ensure compliance to the pre-requisite program requirements. The required HACCP records to be kept at each CCP are written on Form 10 by each brewery in accordance with the brewery requirements.

Monitoring results are documented together with any deviations and corrective action taken. Failure to document the control of a CCP would be a critical departure from the HACCP plan. Verification activities are also to be recorded. Records must specify who recorded the information and must indicate who reviewed and signed off the information.

A record may be in any form (processing chart, written record, computerized record) and show the historical record of the process, the monitoring, the deviations and the corrective actions (including disposition of product) that occurred at the identified CCP. The information contained in the records is used to establish the product's processing profile that would be used if there are any subsequent problems. Accurate records allow for trace back of the actual manufacturing conditions which will aid in troubleshooting if a problem arises.

# HACCP Principle 7 - Establish Record Keeping/ Documentation (Continued)

The importance of records to the HACCP program must be emphasized. The records are an important tool that is   used to ensure that the establishment is following the agreed upon HACCP plan. It will be imperative that the establishment maintain up-to-date, properly filed, and accurate records.

# BAC GENERIC HACCP PROGRAM

# Form 1:

# Product/Process Description

| BAC Generic | Title: Form 1 – Product Description |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

| Process/Product Name: BEER |
| --- |
| 1. Product Name(s) | Beer, Ale, Stout, Malt Liquor As defined in the Food and Drug Regulations B.02.130 to B.02.132. |
| 2. Important Product Characteristics (aw, pH, PRESERVATIVES..) | 3 |
| 3. How it is to be used | Consumer product - Alcoholic beverage |
| 4. Packaging | Glass bottles Lined aluminum bottles Lined cans Stainless steel kegs Plastic bottles (PET etc.) |
| 5. Shelf Life | Shelf Life Information required. |
| 6. Where it will be sold | Government sales provisions apply - licensed retailers, hotels etc. On premise and off premise |
| 7. Labelling Instructions | Food and Drug Regulations (i.e. alcohol content labelling) Consumer Packaging and Labelling Legislative/Regulatory requirements Claims allowed by Health Canada (i.e. energy value) |
| 8. Special Distribution Control | Inspection done on third party carriers and carriers dedicated to food |

# Form 2:

# List of Product Ingredients and Incoming Materials

| BAC Generic | Title: Form 2 - List of Product Ingredients and Incoming Materials |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

| Product Name: BEER |
| --- |
| LIQUID INGREDIENTS | DRY INGREDIENTS (allowable) | PRIMARY PACKAGING MATERIALS |
| Potable water - City Water B C P - Well/ Surface Water B C P - Purchased Water B C | Barley malt B C P Wheat malt B C P Hops BC P Cereal grain e.g. wheat (non-malted), corn, oats, rice B C P | New Glass P Used glass B C P Lined aluminum cans P Lined aluminum bottles P New stainless steel kegs P Used stainless steel kegs None Plastic bottles e.g. PET None Crowns , Closures and Can Ends None |
| OTHER INGREDIENTS (allowable) | OTHER INGREDIENTS (allowable) | OTHER INGREDIENTS (allowable) |
| Caramel C P Dextrin C P Food enzymes C - Amylase, Glucoamylase, Glucanase, Papain, Pentosanase, Protease Stabilizing agents C - Calcium Alginate, Carrageenan, Propylene Glycol Alginate Water preparation agents C - Ammonium Phosphate, dibasic, Calcium Chloride, Calcium Hydroxide, Calcium Sulphate, Citric Acid, Lactic Acid, Magnesium Sulphate, Phosphoric Acid, Sulphuric Acid | Preservatives C - Ascorbic Acid, Calcium Ascorbate, Potassium Metabisulphite, Sodium Metabisulphite Yeast foods C - Manganese Sulphate, Phosphoric Acid, Zinc Sulphate, Ammonium Persulphate (brewers’ yeast) Processing aids B C - Irish Moss Seaweed; Activated Carbon; Magnesium Silicate; Cellulose; China Clay; Diatomaceous Earth; Gelatin; Silica Gel; Polyvinylpolypyrrolidone; Wood Shavings derived from oak, beech, hazelnut or cherry wood; Dimethylpolysiloxane (wort), Hydrogen Peroxide (mash); | Yeast B C Carbohydrate matter, e.g. sucrose, syrup Honey Salt C P Hop oil C P Hop extract C P Carbon dioxide C - Purchased CO2 - Regenerated CO2 Liquid wheat extract C P Nitrogen/ Oxygen/ Compressed Air C |

B/ C/ P = Biological (B) or Chemical (C) or Physical (P) hazard(s) identified.

# Form 3:

# Process Flow Diagram

# Form 4:

# Schematic Diagram

| BAC Generic | Title: Form 4 – Schematic Diagram |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

Note:  Each brewery must be individually assessed at the time of implementation to ensure identified hazards have been addressed.

Schematic Diagram

TO BE COMPLETED –

# Form 5:

# Hazard identification biological hazards

| BAC Generic | Title: Form 5 – Hazard Identification - Biological Hazards |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

| List all biological hazards related to ingredients, incoming material, processing, product flow, etc. | Identified biological hazards (Bacteria, parasites, viruses, etc.) | Controlled at: |
| --- | --- | --- |
| INGREDIENTS |
| LIQUID INGREDIENTS |  |  |
| City Water | Coliform, E. Coli |  |
| Purchased Water | Coliform, E. Coli |  |
| Well/ Lake/ Surface/ Water | Coliform, E. Coli, Parasites |  |
| DRY INGREDIENTS |  |  |
| Barley malt | Micro (fecal contamination from birds, mice) |  |
| Wheat (malted/ non-malted), | Micro (fecal contamination from birds, mice) |  |
| Cereal Grain, e.g. corn, oats, rice | Micro (fecal contamination from birds, mice) |  |
| Hops | Fecal contamination (E. coli) |  |
| OTHER INGREDIENTS |  |  |
| Yeast | Cross contaminated e.g. Salmonella |  |
| Carbohydrate Matter (e.g. sucrose, syrup, honey) | Clostridium |  |
| OTHER INGREDIENTS (Continued) |  |  |
| Yeast | Cross contaminated e.g. Salmonella |  |
| Carbohydrate Matter (e.g. sucrose, syrup, honey) | Clostridium |  |
| Salt | None identified |  |
| Hop Oil | None identified |  |
| Hop Extract | None identified |  |
| Nitrogen/ Oxygen/ Compressed Air Purchased CO2 | None Identified |  |
| Regenerated CO2 | None identified |  |
| Liquid Wheat Extract | None identified |  |
| Caramel | None identified |  |
| Dextrin | None Identified |  |
| Food Enzymes | None identified |  |
| Stabilizing Agents | None identified |  |
| Water preparation agents | None identified |  |
| Preservatives | None Identified |  |
| Yeast Foods | None Identified |  |
| Processing aids Examples – Gelatin, Irish Moss, Wood Shavings | Fecal contamination (e.g. Gelatin, Irish Moss) |  |
| PRIMARY PACKAGING MATERIAL |
| New glass | None identified |  |
| Used glass | Bacteria |  |
| Lined aluminum cans and bottles | None identified |  |
| New Kegs | None identified |  |
| PRIMARY PACKAGING MATERIAL (Continued) |
| Used Kegs | None identified |  |
| Plastic Bottles, e.g. PET | None Identified |  |
| Crowns | None identified |  |
| Closures & Can Ends | None Identified |  |
| PROCESS STEPS |
| PS1- RECEIVING | Micro contamination from receiving open containers (e.g. bird droppings). |  |
| PS2- STORAGE/ HANDLING | Mold growth from improper storage conditions Insect or pest infestation |  |
| PS3 - Brewing |  |  |
| B1 - Receiving | (See PS1 above) |  |
| B2 - Storage | (See PS2 above) |  |
| B3 - Milling | None identified |  |
| B4 - Cereal Cooker | None identified |  |
| B5 - Mashing (Mash Mixer, Mash Cooker) | None identified |  |
| B6 - Lautering (Lauter Tun, Mash Filter removal of spent grains | None identified |  |
| B7 – Holding Tank | None identified |  |
| B8 - Kettle | None identified |  |
| B9 Whirlpool | None identified |  |
| B10 - Wort Cooling (Heat Exchanger) | None identified |  |
| PS4 -Fermentation |  |  |
| Cold Wort (from B10) | None identified |  |
| PROCESS STEPS (Continued) |
| F1 Wort Oxygenation/ Wort Aeration | None identified |  |
| F2 - Fermentation | None identified |  |
| F3 - Cooling | None identified |  |
| F4 - Green Beer | None identified |  |
| PS4 – Sub-Process Yeast Preparation |  |  |
| Y1 – Propagation | None identified |  |
| Y2 – Storage | None identified |  |
| Y3 – Acid Washing | None identified |  |
| PS5 - AGING/ CLARIFICATION/ FILTRATION |  |  |
| A1 - Cooling | None identified |  |
| A2 - Buffer tank | None identified |  |
| A3 - Centrifuge | None identified |  |
| A4 - Buffer tank | None identified |  |
| A5 - Cooling tank | None identified |  |
| A6 - Aging Tank | None identified |  |
| A7 - Secondary Storage | None identified |  |
| A8 - Surge/ buffer Tank | None identified |  |
| A9 – Filtration | None identified |  |
| A10 – Bright Beer Storage | (See PS6 below) |  |
| PS6 – BRIGHT BEER STORAGE | None identified |  |
| PS7 BRIGHT BEER PROCESSING |  |  |
| PS7 (SF) – Sterile Filtration |  |  |
| SF1 - Bright Beer Tank | None identified |  |
| PROCESS STEPS (Continued) |
| SF2 - Filtration | None identified |  |
| SF3 - Sterile Beer Tank | None identified |  |
| PS7(FP) – Flash Pasteurization |  |  |
| FP1 - Bright Beer Tank | None identified |  |
| FP2 - Pasteurization | None identified |  |
| FP3 - Pasteurized Beer Tank | None identified |  |
| PS8 RB – Returned Bottles Prep (Float Glassware Prep) |  |  |
| RB1 - Receiving/ Storage | None identified |  |
| RB2 - De-palletizing | None identified |  |
| RB3- RB4 - De-casing & Inspection (visual) | None identified |  |
| RB5 - Bottle Wash Loading | None identified |  |
| RB6 - Pre-rinse sprays | None identified |  |
| RB7 - Soak Tanks With Caustic | None identified |  |
| RB8 - Hydro Jet Sprays | Spray malfunction and debris is left in bottle (e.g. pathogenic Clostridium, Listeria, Hepatitis (A/B/C) |  |
| RB9- Post-Soak | None identified |  |
| RB10 - External Flush | None identified |  |
| RB11 - Ext. Rinse | None identified |  |
| RB12 - Interior Rinse | None identified |  |
| RB13 - Final Rinse | None identified |  |
| PS8 NB - New Bottles (Glassware) Prep |  |  |
| NB1- NB2 - Receiving & Preliminary Inspection | None identified |  |
| NB3 – NB 6 Storage (Pallet Prep, De-palletize) | None identified |  |
| PROCESS STEPS (Continued) |
| NB7 – Inspection (Human, visual) | None identified |  |
| NB8 - Bottle Loading, | None identified |  |
| NB9 - Bulk Glass Rinser | None identified |  |
| PS8 BT - BOTTLING |  |  |
| BT1 Empty Bottle Inspection (Human or Machine inspection) | None identified |  |
| BT2 – Down Bottle Filler In-Feed Control | None identified |  |
| BT3 – BT5 Filling (Purges , Filling, Fobbing) | None identified |  |
| BT6 - Crowning | None identified |  |
| BT7 – BT 8 Bottle Flush (Full Bottle Wash - external) | None identified |  |
| BT9 – Pasteurize | None identified |  |
| BT10 - Foam Inspection &/or Candling | None identified |  |
| BT11 – Drying (Bottle Drying and Air Knives) | None identified |  |
| BT12 – BT13 Labelling, Coding | None identified |  |
| BT14 – Filled Bottle Inspection | None identified |  |
| BT15 – BT18 Packing & Sealing (Divert to packers, Carton, Case Pack, Sealing) | None identified |  |
| BT19 – BT20 Secondary Code & Inspection (Secondary Packaging, Code/Inspection) | None identified |  |
| BT21 – Palletize | None identified |  |
| PROCESS STEPS (Continued) |
| BT22 - Storage (or Live Load) | None identified |  |
| BT23 - Shipping | None identified |  |
| PS8 (K) - KEGGING |  |  |
| K1 - Receiving (See PS1) | None identified |  |
| K2 – K3 Storage & Handling , De-palletizing (See PS2) | None identified |  |
| K4 - External Inspection | None identified |  |
| K5 – K6 External Cleaning (Ext Wash/Inspection) | None identified |  |
| K7 – Racking | None identified |  |
| K8 – K12 Internal Cleaning (Purge, Flush, Wash, Purge, Rinse) | None identified |  |
| K13 - Sterilize & Hold | None identified |  |
| K14 – K 15 Purge to Empty & Counter pressure | None identified |  |
| K 16 - K17 Barnes Neck Sanitize & Inspect | None identified |  |
| K18 - Filling | None identified |  |
| K19 – K 21 Barnes Neck, Wash & Sanitize | None identified |  |
| K22 - Dust Cap | None identified |  |
| K23 - Air Dry | None identified |  |
| K24 - Product Code Applied | None identified |  |
| K25 – K 26 Weigh (In-line weighing) & Palletize | None identified |  |
| K27 - Storage | None identified |  |
| K28 - Shipping | None identified |  |
| PROCESS STEPS (Continued) |
| PS8 (C) - CANNING |  |  |
| C1 - Receiving | None identified |  |
| C2 - Storage & Handling | Bacterial contamination from leaking roof or pipes |  |
| C3 – C 4 De-palletize / Pallet ID (Collect & Timestamp Can Pallet ID, De-palletize) | None identified |  |
| C5 - Online visual inspection | None identified |  |
| C6 - Primary code applied | None identified |  |
| C7 - Bulk in-line rinser | None identified |  |
| C8 – C 10 Filling (pre-evacuation & beer fill) | None identified |  |
| C11 – C13 Seaming | None identified |  |
| C14 - External Can Flush | None identified |  |
| C15 – Pasteurizer | None identified |  |
| C16 – C17 Drying | None identified |  |
| C18 - Fill Height Inspection | None identified |  |
| C19 - Divert to Packers | None identified |  |
| C20 - Hi-Cone Machine | None identified |  |
| C21 - Case Packers | None identified |  |
| C22 – Inspection (Human, visual) Inspection | None identified |  |
| C23 – C24 Tray Machine & Code | None identified |  |
| C25 – Palletize | None identified |  |
| C26 - Storage (or Live Load) | None identified |  |
| PROCESS STEPS (Continued) |
| C27 – Shipping | None identified |  |
| PS8 T - TANKERING |  |  |
| T1 - Empty Tanker (Receiving) | None identified |  |
| T2 - Tanker Washing/ Rinsing | None identified |  |
| T3 - Tanker Purging | None identified |  |
| T4 - Tanker Filling/ Loading | Insect or pest infestation of hoses |  |
| T5 – Tanker Shipping | None identified |  |
| T6 – T7 Full Tanker Receiving & Unloading | Insect or pest infestation of hoses |  |

| Date: | Approved by: |
| --- | --- |

# Form 6:

# Hazard identification chemical hazards

| BAC Generic | Title: Form 6 – Hazard Identification - Chemical Hazards |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

| List all chemical hazards related to ingredients, incoming material, processing, product flow, etc. | Identified chemical hazards | Controlled at: |
| --- | --- | --- |
| INGREDIENTS |
| LIQUID INGREDIENTS |  |
| City Water | Pesticides, Heavy metals |  |
| Purchased Water | Cleaning chemicals, cross contamination from previous load |  |
| Well/ Lake/ Surface/ Water | Pesticides, Heavy metals |  |
| DRY INGREDIENTS |  |
| Barley malt | Pesticides, Mycotoxins, Allergen (cross-contamination from carrier), NDMA |  |
| Wheat (malted/ non-malted), | Pesticides, Mycotoxins, Allergen, NDMA |  |
| Cereal Grain, e.g. corn, oats, rice | Pesticides, Mycotoxins, Allergen (cross-contamination from carrier), NDMA |  |
| Hops | Pesticides, Mycotoxins |  |
| OTHER INGREDIENTS |  |  |
| Yeast | Heavy Metals, cleaning chemicals (used in tankers) |  |
| Carbohydrate Matter (e.g. sucrose, syrup, honey) | Antibiotic residue, heavy metal (honey) |  |
| Salt | Non-food grade |  |
| Hop Oil | Residual solvents, Non-food grade |  |

| OTHER INGREDIENTS (Continued) |
| --- |
| Hop Extract | Residual solvents, Non-food grade |  |
| Nitrogen/ Oxygen/ Compressed Air Purchased CO2 | Chemical non-volatile gases, Non-food grade |  |
| Regenerated CO2 | Contamination from oil (from the compressor) |  |
| Liquid Wheat Extract | Allergen |  |
| Caramel | Non-food grade |  |
| Dextrin | Non-food grade |  |
| Food Enzymes | Non-food grade |  |
| Stabilizing Agents | Heavy metals, Non-food grade |  |
| Water preparation agents | Heavy metals, Non-food grade |  |
| Preservatives | Allergens (Sulphites), Non-food grade |  |
| Yeast Foods | Heavy metals, Non-food grade |  |
| Processing aids Examples – Gelatin, Irish Moss, Wood Shavings | Heavy metals, Non-food grade |  |
| PRIMARY PACKAGING MATERIAL |
| New glass | None identified |  |
| Used glass | Lubricants, mycotoxins |  |
| Lined aluminum cans and bottles | None identified |  |
| New Kegs | None identified |  |
| Used Kegs | None identified |  |
| PRIMARY PACKAGING MATERIAL (Continued) |
| Plastic Bottles, e.g. PET | None identified |  |
| Crowns | None identified |  |
| Closures & Can Ends | None identified |  |
| PROCESS STEPS |
| PS1- RECEIVING | Chemical – Contamination from truck (damage, leaks, odors) |  |
| PS2- STORAGE/ HANDLING | Chemical - Cross-contamination from allergens (e.g. wheat) |  |
| PS3 - Brewing |  |  |
| B1 - Receiving | (See PS1 above) |  |
| B2 - Storage | (See PS2 above) |  |
| B3 - Milling | Chemical – Allergen cross-contamination (e.g. from residues in the mill) |  |
| B4 - Cereal Cooker | None identified |  |
| B5 - Mashing (Mash Mixer, Mash Cooker) | None identified |  |
| B6 - Lautering (Lauter Tun, Mash Filter removal of spent grains | None identified |  |
| B7 – Holding Tank | None identified |  |
| B8 - Kettle | None identified |  |
| B9 Whirlpool | None identified |  |
| B10 - Wort Cooling (Heat Exchanger) | None identified |  |
| PS4 -Fermentation |  |  |
| Cold Wort (from B10) | None identified |  |
| F1 Wort Oxygenation/ Wort Aeration | None identified |  |
| PRIMARY PACKAGING MATERIAL (Continued) |
| F2 - Fermentation | None identified |  |
| F3 - Cooling | Coolant leak |  |
| F4 - Green Beer | None identified |  |
| PS4 – Sub-Process Yeast Preparation |  |  |
| Y1 – Propagation | None identified |  |
| Y2 – Storage | None identified |  |
| Y3 – Acid Washing | None identified |  |
| PS5 - AGING/ CLARIFICATION/ FILTRATION |  |  |
| A1 - Cooling | Coolant leak |  |
| A2 - Buffer tank | None identified |  |
| A3 - Centrifuge | None identified |  |
| A4 - Buffer tank | None identified |  |
| A5 - Cooling tank | Coolant leak |  |
| A6 - Aging Tank | Coolant leak |  |
| A7 - Secondary Storage | Coolant leak Sulphites as an allergen |  |
| A8 - Surge/ buffer Tank | Sulphites as an allergen |  |
| A9 – Filtration | Sulphites as an allergen |  |
| A10 – Bright Beer Storage | (See PS6 below) |  |
| PS6 – BRIGHT BEER STORAGE | Coolant leak Sulphites as an allergen Cleaning chemicals |  |
| PS7 BRIGHT BEER PROCESSING |  |  |
| PS7 (SF) – Sterile Filtration |  |  |
| SF1 - Bright Beer Tank | Coolant leak Sulphites as an allergen Cleaning chemicals |  |
| PRIMARY PACKAGING MATERIAL (Continued) |
| SF2 - Filtration | Sulphites as an allergen |  |
| SF3 - Sterile Beer Tank | None identified |  |
| PS7(FP) – Flash Pasteurization |  |  |
| FP1 - Bright Beer Tank | Coolant leak Sulphites as an allergen Cleaning chemicals |  |
| FP2 - Pasteurization | Contamination from coolant |  |
| FP3 - Pasteurized Beer Tank | None identified |  |
| PS8 RB – Returned Bottles Prep (Float Glassware Prep) |  |  |
| RB1 - Receiving/ Storage | None identified |  |
| RB2 - De-palletizing | None identified |  |
| RB3- RB4 - De-casing & Inspection (visual) | None identified |  |
| RB5 - Bottle Wash Loading | None identified |  |
| RB6 - Pre-rinse sprays | None identified |  |
| RB7 - Soak Tanks With Caustic | Too concentrated, too low, no caustic, wrong chemical Bottle unable to drain |  |
| RB8 - Hydro Jet Sprays | Bottle unable to drain |  |
| RB9- Post-Soak | Bottle unable to drain |  |
| RB10 - External Flush | None identified |  |
| RB11 - Ext. Rinse | None identified |  |
| RB12 - Interior Rinse | Spray malfunction Bottle plugged unable to drain |  |
| RB13 - Final Rinse | Bottle unable to drain |  |
| PS8 NB - New Bottles (Glassware) Prep |  |  |
| PRIMARY PACKAGING MATERIAL (Continued) |
| NB1- NB2 - Receiving & Preliminary Inspection | None identified |  |
| NB3 – NB 6 Storage (Pallet Prep, De-palletize) | None identified |  |
| NB7 – Inspection (Human, visual) | None identified |  |
| NB8 - Bottle Loading, | None identified |  |
| NB9 - Bulk Glass Rinser | Contaminated air, sanitizing spray |  |
| PS8 BT - BOTTLING |  |  |
| BT1 Empty Bottle Inspection (Human or Machine inspection) | MACHINE: Failure of the system to detect residual liquid and caustic HUMAN: Failure of personnel to detect residual liquid |  |
| BT2 – Down Bottle Filler In-Feed Control | None identified |  |
| BT3 – BT5 Filling (Purges , Filling, Fobbing) | CIP chemicals in bottle |  |
| BT6 - Crowning | Lubricants |  |
| BT7 – BT 8 Bottle Flush (Full Bottle Wash - external) | None identified |  |
| BT9 – Pasteurize | None identified |  |
| BT10 - Foam Inspection &/ or Candling | None identified |  |
| BT11 – Drying (Bottle Drying and Air Knives) | None identified |  |
| BT12 – BT13 Labelling, Coding | Product not coded or not correctly coded |  |
| BT14 – Filled Bottle Inspection | None identified |  |
| PRIMARY PACKAGING MATERIAL (Continued) |
| BT15 – BT18 Packing & Sealing (Divert to packers, Carton, Case Pack, Sealing) | None identified |  |
| BT19 – BT20 Secondary Code & Inspection (Secondary Packaging, Code/Inspection) | Product not coded or not correctly coded |  |
| BT21 – Palletize | None identified |  |
| BT22 - Storage (or Live Load) | None identified |  |
| BT23 - Shipping | None identified |  |
| PS8 (K) - KEGGING |  |  |
| K1 - Receiving (See PS1) | None identified |  |
| K2 – K3 Storage & Handling , De-palletizing (See PS2) | None identified |  |
| K4 - External Inspection | None identified |  |
| K5 – K6 External Cleaning (Ext Wash/Inspection) | Old codes not effectively removed |  |
| K7 – Racking | None identified |  |
| K8 – K12 Internal Cleaning (Purge, Flush, Wash, Purge, Rinse) | Automated Cleaning solution not effectively removed. Manual Cleaning solution not effectively removed. |  |
| K13 - Sterilize & Hold | None identified |  |
| K14 – K 15 Purge to Empty & Counter pressure | None identified |  |
| K 16 - K17 Barnes Neck Sanitize & Inspect | None identified |  |
| K18 - Filling | CIP solution |  |
| PRIMARY PACKAGING MATERIAL (Continued) |
| K19 – K 21 Barnes Neck, Wash & Sanitize | None identified |  |
| K22 - Dust Cap | None identified |  |
| K23 - Air Dry | None identified |  |
| K24 - Product Code Applied | Incorrect or missing code |  |
| K25 – K 26 Weigh (In-line weighing) & Palletize | None identified |  |
| K27 - Storage | None identified |  |
| K28 - Shipping | None identified |  |
| PS8 (C) - CANNING |  |  |
| C1 - Receiving | None identified |  |
| C2 - Storage & Handling | Contamination from leaking roof or pipes |  |
| C3 – C 4 De-palletize / Pallet ID (Collect & Timestamp Can Pallet ID, De-palletize) | Incorrect or missing code on pallet |  |
| C5 - Online visual inspection | None identified |  |
| C6 - Primary code applied | Incorrect or missing code – |  |
| C7 - Bulk in-line rinser | Chemicals from compressed air or water |  |
| C8 – C 10 Filling (pre-evacuation & beer fill) | None identified |  |
| C11 – C13 Seaming | Chemicals, Lubricants |  |
| C14 - External Can Flush | None identified |  |
| C15 – Pasteurizer | None identified |  |
| C16 – C17 Drying | None identified |  |
| C18 - Fill Height Inspection | None identified |  |
| PRIMARY PACKAGING MATERIAL (Continued) |
| C19 - Divert to Packers | None identified |  |
| C20 - Hi-Cone Machine | None identified |  |
| C21 - Case Packers | None identified |  |
| C22 – Inspection (Human, visual) Inspection | None identified |  |
| C23 – C24 Tray Machine & Code | Incorrect or missing code |  |
| C25 – Palletize | None identified |  |
| C26 - Storage (or Live Load) | None identified |  |
| C27 – Shipping | None identified |  |
| PS8 T - TANKERING |  |  |
| T1 - Empty Tanker (Receiving) | Cleaning chemicals and/ or sanitizer |  |
| T2 - Tanker Washing/ Rinsing | Cleaning chemicals and/ or sanitizer |  |
| T3 - Tanker Purging | Contaminated CO2 |  |
| T4 - Tanker Filling/ Loading | Cross contamination from using hose on non-food material |  |
| T5 – Tanker Shipping | None identified |  |
| T6 – T7 Full Tanker Receiving & Unloading | Cross contamination with chemicals from the supplier Cross contamination from using hose on non-food material |  |
| Date: | Approved by: |

# Form 7:

# Hazard identification physical hazards

| BAC Generic | Title: Form 7 – Hazard Identification - Physical Hazards |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

| List all physical hazards related to ingredients, incoming material, processing, product flow, etc. | Identified physical hazards | Controlled at: |
| --- | --- | --- |
| INGREDIENTS |
| LIQUID INGREDIENTS |  |  |
| City Water | Silt |  |
| Purchased Water | None identified |  |
| Well/ Lake/ Surface/ Water | Silt |  |
| DRY INGREDIENTS |  |  |
| Barley malt | Glass, Metal |  |
| Wheat (malted/ non-malted), | Glass, Metal |  |
| Cereal Grain, e.g. corn, oats, rice | Glass, Metal |  |
| Hops | Insects, metal |  |
| OTHER INGREDIENTS |  |  |
| Yeast | None identified |  |
| Carbohydrate Matter (e.g. sucrose, syrup, honey) | None identified |  |
| Salt | Rocks |  |
| Hop Oil | Plastic |  |
| Hop Extract | Plastic |  |
| Nitrogen/ Oxygen/ Compressed Air Purchased CO2 | None identified |  |
| OTHER INGREDIENTS (Continued) |
| Regenerated CO2 | None identified |  |
| Liquid Wheat Extract | Plastic (from packaging) |  |
| Caramel | Plastic (from container) |  |
| Dextrin | Plastic (from container) |  |
| Food Enzymes | None identified |  |
| Stabilizing Agents | None identified |  |
| Water preparation agents | None identified |  |
| Preservatives | None identified |  |
| Yeast Foods | None identified |  |
| Processing aids Examples – Gelatin, Irish Moss, Wood Shavings | None identified |  |
| PRIMARY PACKAGING MATERIAL |
| New glass | Critical Glass Defects , Glass |  |
| Used glass | Critical Glass Defects , Dirt, Dust, Glass, Syringes, Medical Patches |  |
| Lined aluminum cans and bottles | Metal Shavings |  |
| New Kegs | Metal Shavings |  |
| Used Kegs | None identified |  |
| Plastic Bottles, e.g. PET | None identified |  |
| Crowns | None identified |  |
| Closures & Can Ends | None identified |  |
| PROCESS STEPS |
| PS1- RECEIVING | Pests in hoses used for transferring material, Bulk Receiving |  |
| PROCESS STEPS (Continued) |
| PS2- STORAGE/ HANDLING | Insect or pest infestation |  |
| PS3 - Brewing |  |  |
| B1 - Receiving | (See PS1 above) |  |
| B2 - Storage | (See PS2 above) |  |
| B3 - Milling | None identified |  |
| B4 - Cereal Cooker | None identified |  |
| B5 - Mashing (Mash Mixer, Mash Cooker) | None identified |  |
| B6 - Lautering (Lauter Tun, Mash Filter removal of spent grains | None identified |  |
| B7 – Holding Tank | None identified |  |
| B8 - Kettle | None identified |  |
| B9 Whirlpool | None identified |  |
| B10 - Wort Cooling (Heat Exchanger) | None identified |  |
| PS4 -Fermentation |  |  |
| Cold Wort (from B10) | None identified |  |
| F1 Wort Oxygenation/ Wort Aeration | None identified |  |
| F2 - Fermentation | None identified |  |
| F3 - Cooling |  |  |
| F4 - Green Beer | None identified |  |
| PS4 – Sub-Process Yeast Preparation |  |  |
| Y1 – Propagation | None identified |  |
| Y2 – Storage | None identified |  |
| PROCESS STEPS (Continued) |
| Y3 – Acid Washing | None identified |  |
| PS5 - AGING/ CLARIFICATION/ FILTRATION |  |  |
| A1 - Cooling |  |  |
| A2 - Buffer tank | None identified |  |
| A3 - Centrifuge | None identified |  |
| A4 - Buffer tank | None identified |  |
| A5 - Cooling tank | None identified |  |
| A6 - Aging Tank | None identified |  |
| A7 - Secondary Storage | None identified |  |
| A8 - Surge/ buffer Tank | None identified |  |
| A9 – Filtration | None identified |  |
| A10 – Bright Beer Storage | None identified |  |
| PS6 – BRIGHT BEER STORAGE | None identified |  |
| PS7 BRIGHT BEER PROCESSING |  |  |
| PS7 (SF) – Sterile Filtration |  |  |
| SF1 - Bright Beer Tank | None identified |  |
| SF2 - Filtration | None identified |  |
| SF3 - Sterile Beer Tank | None identified |  |
| PS7(FP) – Flash Pasteurization |  |  |
| FP1 - Bright Beer Tank | None identified |  |
| FP2 - Pasteurization | None identified |  |
| FP3 - Pasteurized Beer Tank | None identified |  |
| PROCESS STEPS (Continued) |
| PS8 RB – Returned Bottles Prep (Float Glassware Prep) |  |  |
| RB1 - Receiving/ Storage | Damage to bottles |  |
| RB2 - De-palletizing | Damage to bottles |  |
| RB3- RB4 - De-casing & Inspection (visual) | Damage to bottles |  |
| RB5 - Bottle Wash Loading | Damage to bottles |  |
| RB6 - Pre-rinse sprays | Damage to bottles (e.g. Temperature shock due to storage) |  |
| RB7 - Soak Tanks With Caustic | Damage to bottles |  |
| RB8 - Hydro Jet Sprays | Damage to bottles Bottle contains foreign object (spray malfunction) Bottle contains foreign object (plugged but sprays cannot clear object) |  |
| RB9- Post-Soak | Damage to bottles (e.g. Temperature shock) Bottle plugged |  |
| RB10 - External Flush | Damage to bottles (e.g. Temperature shock) |  |
| RB11 - Ext. Rinse | Damage to bottles (e.g. Temperature shock) |  |
| RB12 - Interior Rinse | Damage to bottles Bottle contains foreign object (spray malfunction) Bottle contains foreign object (plugged but sprays cannot clear object) |  |

| PROCESS STEPS (Continued) |
| --- |
| RB13 - Final Rinse | Damage to bottles Bottle contains foreign object (spray malfunction) Bottle contains foreign object (plugged but sprays cannot clear object) |  |
| PS8 NB - New Bottles (Glassware) Prep |  |  |
| NB1- NB2 - Receiving & Preliminary Inspection | Damage to bottles |  |
| NB3 – NB 6 Storage (Pallet Prep, De-palletize) | Damage to bottles |  |
| NB7 – Inspection (Human, visual) | Missed critical glass defects |  |
| NB8 - Bottle Loading, | Damage to bottles |  |
| NB9 - Bulk Glass Rinser | Spray malfunction (e.g. plugged sprays) |  |
| PS8 BT - BOTTLING |  |  |
| BT1 Empty Bottle Inspection (Human or Machine inspection) | MACHINE: Failure of the system to detect foreign matter, glass defects, bottle damage HUMAN: Failure of personnel to detect foreign matter, glass defects, glass damage |  |
| BT2 – Down Bottle Filler In-Feed Control | Glass inclusions from breakage of down bottle at filler in-feed |  |
| BT3 – BT5 Filling (Purges , Filling, Fobbing) | Chipping of bottles (e.g. from filling equipment), glass inclusion Auto-Flush Burst bottle leading to glass inclusion Manual Flush Burst bottle leading to glass inclusion |  |
| PROCESS STEPS (Continued) |
| BT6 - Crowning | Bottle finish damage (leading to glass inclusions) |  |
| BT7 – BT 8 Bottle Flush (Full Bottle Wash - external) | None identified |  |
| BT9 – Pasteurize | None identified |  |
| BT10 - Foam Inspection &/or Candling | HUMAN: Physical – Failure to detect foreign matter (including glass) MACHINE: Physical – Failure to detect foreign matter (including glass) |  |
| BT11 – Drying (Bottle Drying and Air Knives) | None identified |  |
| BT12 – BT13 Labelling, Coding | Product not coded or not correctly coded |  |
| BT14 – Filled Bottle Inspection | None identified |  |
| BT15 – BT18 Packing & Sealing (Divert to packers, Carton, Case Pack, Sealing) | None identified |  |
| BT19 – BT20 Secondary Code & Inspection (Secondary Packaging, Code/Inspection) | Product not coded, or not correctly coded |  |
| BT21 – Palletize | None identified |  |
| BT22 - Storage (or Live Load) | None identified |  |
| BT23 - Shipping | None identified |  |
| PS8 (K) - KEGGING |  |  |
| K1 - Receiving (See PS1) | None identified |  |
| PROCESS STEPS (Continued) |
| K2 – K3 Storage & Handling , De-palletizing (See PS2) | None identified |  |
| K4 - External Inspection | None identified |  |
| K5 – K6 External Cleaning (Ext Wash/Inspection) | Old codes not effectively removed |  |
| K7 – Racking | None identified |  |
| K8 – K12 Internal Cleaning (Purge, Flush, Wash, Purge, Rinse) | None identified |  |
| K13 - Sterilize & Hold | None identified |  |
| K14 – K 15 Purge to Empty & Counter pressure | None identified |  |
| K 16 - K17 Barnes Neck Sanitize & Inspect | None identified |  |
| K18 - Filling | None identified |  |
| K19 – K 21 Barnes Neck, Wash & Sanitize | None identified |  |
| K22 - Dust Cap | None identified |  |
| K23 - Air Dry | None identified |  |
| K24 - Product Code Applied | Incorrect or missing code |  |
| K25 – K 26 Weigh (In-line weighing) & Palletize | None identified |  |
| K27 - Storage | None identified |  |
| K28 - Shipping | None identified |  |
| PS8 (C) - CANNING |  |  |
| C1 - Receiving | None identified |  |
| C2 - Storage & Handling | None identified |  |

| PROCESS STEPS (Continued) |
| --- |
| C3 – C 4 De-palletize / Pallet ID (Collect & Timestamp Can Pallet ID, De-palletize) | Incorrect or missing code on pallet |  |
| C5 - Online visual inspection | None identified |  |
| C6 – Primary code applied | Incorrect or missing code – |  |
| C7 - Bulk in-line rinser | None identified |  |
| C8 – C 10 Filling (pre-evacuation & beer fill) | None identified |  |
| C11 – C13 Seaming | None identified |  |
| C14 - External Can Flush | None identified |  |
| C15 – Pasteurizer | None identified |  |
| C16 – C17 Drying | None identified |  |
| C18 - Fill Height Inspection | None identified |  |
| C19 - Divert to Packers | None identified |  |
| C20 - Hi-Cone Machine | None identified |  |
| C21 - Case Packers | None identified |  |
| C22 – Inspection (Human, visual) Inspection | None identified |  |
| C23 – C24 Tray Machine & Code | Incorrect or missing code |  |
| C25 – Palletize | None identified |  |
| C26 - Storage (or Live Load) | None identified |  |
| C27 – Shipping | None identified |  |
| PROCESS STEPS (Continued) |
| PS8 T - TANKERING |  |  |
| T1 - Empty Tanker (Receiving) | None identified |  |
| T2 - Tanker Washing/ Rinsing | None identified |  |
| T3 - Tanker Purging | None identified |  |
| T4 - Tanker Filling/ Loading | None identified |  |
| T5 – Tanker Shipping | None identified |  |
| T6 – T7 Full Tanker Receiving & Unloading | None identified |  |

| Date: | Approved by: |
| --- | --- |

# Form 8:

# Critical Control Points

| BAC Generic | Title: Form 8 – Critical Control Points |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

| Incoming material/ process step/ hazards on schematic diagram | Category and identified hazard. | Determine if fully controlled by Pre-requisite program. *If “yes” = indicate “Pre-requisite Program” and proceed to next identified hazard. *If “no” = proceed to question1 (Q1). | Q1. Could a control measure(s) be used by the operator at any process step? If NO = not a CCP + identification on how this hazard will be controlled before and after the process + proceed to the next identified hazard If YES = description + next question (Q2) | Q2. Is it likely that contamination with the identified hazard could occur in excess of the acceptable level or could increase to an unacceptable level? If NO = not a CCP + proceed to the next identified hazard If YES = next question (Q3) | Q3. Is this process step specifically designed to eliminate/reduce the likely occurrence of the identified hazard to an acceptable level? If NO = next question (Q4) If YES = CCP + go to last column | Q4. Will a subsequent step eliminate the identified hazard or reduce likely occurrence to an acceptable level? If NO = CCP + go to last column If YES = not a CCP + identify subsequent step + proceed to the next identified hazard | CCP Number + proceed to next identified hazard |
| --- | --- | --- | --- | --- | --- | --- | --- |
| INGREDIENTS |
| LIQUID INGREDIENTS |
| WATER |
| City Water | Biological - Coliform, E. Coli Chemical - Pesticides, Heavy metals Physical – Silt | PP – Premises, Water Quality (BAC A4.1) – All Hazards |  |  |  |  |  |
| Purchased Water | Biological - Coliform, E. Coli Chemical – Cleaning chemicals, cross contamination from previous load | PP – Premises, Water Quality (BAC A4.1) PP - Transportation Receiving & Storage (BAC B1.1) - COA/ Supplier Audits |  |  |  |  |  |
| Well/ Lake/ Surface/ Water | Biological - Coliform, E. Coli, Parasites Chemical - Pesticides, Heavy metals Physical – Silt | PP – Premises, Water Quality (BAC A4.1) |  |  |  |  |  |
| DRY INGREDIENTS |
| Barley malt | Biological – Micro (faecal contamination from birds, mice) Chemical – Pesticides, Mycotoxins, Allergen (cross-contamination from carrier), NDMA Physical – Glass, Metal | PP - Transportation Receiving & Storage (BAC B1.1) - COA from supplier PP - Transportation Receiving & Storage (BAC B1.1) - COA / Letter of Guarantee PP - Transportation Receiving & Storage (BAC B1.1) - Receiving Inspection (screens, magnets) |  |  |  |  |  |
| Wheat (malted/ non-malted), | Biological – Micro (faecal contamination from birds, mice) Chemical – Pesticides, Mycotoxins, Allergen, NDMA Physical – Glass, Metal | PP - Transportation Receiving & Storage (BAC B1.1) + COA from supplier PP - Transportation Receiving & Storage (BAC B1.1) + COA / Letter of Guarantee, Allergen Management Program PP - Transportation Receiving & Storage (BAC B1.1) + Receiving Inspection (screens, magnets) |  |  |  |  |  |
| Cereal Grain, e.g. corn, oats, rice | Biological – Micro (faecal contamination from birds, mice) Chemical – Pesticides, Mycotoxins, Allergen (cross-contamination from carrier), NDMA Physical – Glass, Metal | PP - Transportation Receiving & Storage (BAC B1.1) + COA from supplier PP - Transportation Receiving & Storage (BAC B1.1) + COA / Letter of Guarantee, Allergen Management Program PP - Transportation Receiving & Storage (BAC B1.1) + Receiving Inspection (screens, magnets) |  |  |  |  |  |
| Hops | Biological – Faecal contamination (E. coli) Chemical – Pesticides, Mycotoxins Physical – Insects, metal | PP - Transportation Receiving & Storage (BAC B1.1) + COA PP – Transportation, Receiving & Storage (BAC B1.1) + COA PP - Transportation Receiving & Storage (BAC B1.1) + COA, Inspection |  |  |  |  |  |
| OTHER INGREDIENTS |
| Yeast | Biological – Cross contaminated e.g. Salmonella Chemical – Heavy Metals, cleaning chemicals (used in tankers) Physical – None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA PP – Transportation, Receiving & Storage (BAC B1.1) + COA, Wash Tickets |  |  |  |  |  |
| Carbohydrate Matter (e.g. sucrose, syrup, honey) | Biological – Clostridium Chemical – Antibiotic residue, heavy metal (honey) Physical – None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA PP – Transportation, Receiving & Storage (BAC B1.1) + COA |  |  |  |  |  |
| Salt | Biological – None identified Chemical – Non-food grade Physical – Rocks | PP – Transportation, Receiving & Storage (BAC B1.1) + COA (Partially Controlled) PP – Transportation, Receiving & Storage (BAC B1.1) + Inspection | Yes – Screens, filters, inspection | No |  |  |  |
| Hop Oil | Biological – None identified Chemical – Residual solvents, Non-food grade Physical – Plastic | + PP – Transportation, Receiving & Storage (BAC B1.1) COA PP – Transportation, Receiving & Storage (BAC B1.1) + COA, Inspection |  |  |  |  |  |
| Hop Extract | Biological – None identified Chemical – Residual solvents, Non-food grade Physical – Plastic | PP – Transportation, Receiving & Storage (BAC B1.1) + COA PP – Transportation, Receiving & Storage (BAC B1.1) + COA, Inspection |  |  |  |  |  |
| Nitrogen/ Oxygen/ Compressed Air Purchased CO2 | Biological – None Identified Chemical – Chemical non-volatile gases, Non-food grade Physical – None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA, QC Testing |  |  |  |  |  |
| Regenerated CO2 | Chemical - Contamination from oil (from the compressor) | PP - Equipment (BAC C1.2) |  |  |  |  |  |
| Liquid Wheat Extract | Biological – None identified Chemical – Allergen Physical – Plastic (from packaging) | Allergen Management Program PP – Transportation, Receiving & Storage (BAC B1.1) + COA |  |  |  |  |  |
| Caramel | Biological – None identified Chemical – Non-food grade Physical – Plastic (from container) | PP – Transportation, Receiving & Storage (BAC B1.1) + COA PP – Transportation, Receiving & Storage (BAC B1.1) + COA |  |  |  |  |  |
| Dextrin | Biological – None identified Chemical – Non-food grade Physical – Plastic (from container) | PP – Transportation, Receiving & Storage (BAC B1.1) + COA PP – Transportation, Receiving & Storage (BAC B1.1) + COA |  |  |  |  |  |
| Food Enzymes | Biological – None identified Chemical – Non-food grade Physical – None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |  |  |  |  |  |
| Stabilizing Agents | Biological – None identified Chemical – Heavy metals, Non-food grade + COA Physical – None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |  |  |  |  |  |
| Water preparation agents | Biological – None identified Chemical – Heavy metals, Non-food grade + COA Physical – None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |  |  |  |  |  |
| Preservatives | Biological – None identified Chemical – Allergens (Sulphites), Non-food grade Physical – None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA, Allergen Management Program |  |  |  |  |  |
| Yeast Foods | Biological – None identified Chemical – Heavy metals, Non-food grade Physical – None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA, |  |  |  |  |  |
| Processing aids Examples – Gelatin, Irish Moss, Wood Shavings | Biological – Faecal contamination (e.g. Gelatin, Irish Moss) Chemical – Heavy metals, Non-food grade Physical – None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA PP – Transportation, Receiving & Storage (BAC B1.1) + COA |  |  |  |  |  |
| PRIMARY PACKAGING MATERIAL | Q1 | Q2 | Q3 | Q4 |  |
| New glass | Biological- None identified Chemical – None identified Physical - Critical Glass Defects , Glass | (Partially Controlled) PP – Transportation, Receiving & Storage (BAC B1.1) +COA, Inspection | Yes – Bottle Rinse | Yes | No | Yes- Empty Bottle Inspection |  |
| Used glass | Biological- Bacteria Chemical – Lubricants, mycotoxins Physical - Critical Glass Defects , Dirt, Dust, Glass, Syringes, Medical Patches, | No (Partially Controlled) PP – Transportation, Receiving & Storage (BAC B1.1) + Inspection, No | Yes – Pasteurization Yes – Bottle Rinse Yes – Bottle Wash | No (no pathogens known to survive in final product due to properties of beer, e.g. low pH, alcohol content see Form 1) Yes Yes | No No | Yes – Empty Bottle Inspection/ RLD Yes – Empty Bottle Inspection |  |
| Lined aluminum cans and bottles | Biological – None identified Chemical – None identified Physical – Metal Shavings | (Partially Controlled) PP – Transportation, Receiving & Storage (BAC B1.1) +COA | Yes – Rinse | No |  |  |  |
| New Kegs | Biological – None identified Chemical – None identified Physical – Metal Shavings | (Partially Controlled) Rinse | Yes - Rinse | No |  |  |  |
| Used Kegs | Biological – None identified Chemical – None identified Physical – None identified |  |  |  |  |  |  |
| Plastic Bottles, e.g. PET | Biological – None identified Chemical – None identified Physical – None identified |  |  |  |  |  |  |
| Crowns | Biological – None identified Chemical – None identified Physical – None identified |  |  |  |  |  |  |
| Closures & Can Ends | Biological – None identified Chemical – None identified Physical – None identified |  |  |  |  |  |  |

| PROCESS STEPS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| PS1- RECEIVING | Biological – Micro contamination from receiving open containers (e.g. bird droppings). Chemical – Contamination from truck (damage, leaks, odors) Physical – Pests in hoses used for transferring material, Bulk Receiving | PP – Premises (BAC A1.1 & BAC A2.1) PP - Pest Control (BAC E2.1) PP – Transportation, Receiving & Storage (BAC B1.1) PP – Transportation, Receiving & Storage (BAC B1.1) + Seal Integrity PP - Pest Control (BAC E2.1) PP – Personnel (BAC D1.2) + Training |  |  |  |  |  |
| PS2- STORAGE/ HANDLING | Biological - Mold growth from improper storage conditions Chemical - Cross-contamination from allergens (e.g. wheat) Physical & Biological - Insect or pest infestation | PP - Premises (BAC A2.1) PP - Sanitation (BAC E1.1) Allergen Management Program PP - Pest Control (BAC E2.1) |  |  |  |  |  |
| PS3 - Brewing |  |  |  |  |  |  |  |
| B1 - Receiving | (See PS1 above) |  |  |  |  |  |  |
| B2 - Storage | (See PS2 above) |  |  |  |  |  |  |
| B3 - Milling | Chemical – Allergen cross-contamination (e.g. from residues in the mill) | PP - Sanitation (BAC E1.1) Allergen Management Program |  |  |  |  |  |
| B4 - Cereal Cooker | None identified |  |  |  |  |  |  |
| B5 - Mashing (Mash Mixer, Mash Cooker) | None identified |  |  |  |  |  |  |
| B6 - Lautering (Lauter Tun, Mash Filter removal of spent grains | None identified |  |  |  |  |  |  |
| B7 – Holding Tank | None identified |  |  |  |  |  |  |
| B8 - Kettle | None identified |  |  |  |  |  |  |
| B9 Whirlpool | None identified |  |  |  |  |  |  |
| B10 - Wort Cooling (Heat Exchanger) | None identified |  |  |  |  |  |  |
| PS4 -Fermentation |  |  |  |  |  |  |  |
| Cold Wort (from B10) | None identified |  |  |  |  |  |  |
| F1 Wort Oxygenation/ Wort Aeration | None identified |  |  |  |  |  |  |
| F2 - Fermentation | None identified |  |  |  |  |  |  |
| F3 - Cooling | Chemical - Coolant leak | PP – Equipment (BAC C1.2) |  |  |  |  |  |
| F4 - Green Beer | None identified |  |  |  |  |  |  |
| PS4 – Sub-Process Yeast Preparation |  |  |  |  |  |  |  |
| Y1 – Propagation | None identified |  |  |  |  |  |  |
| Y2 – Storage | None identified |  |  |  |  |  |  |
| Y3 – Acid Washing | None identified |  |  |  |  |  |  |
| PS5 - AGING/ CLARIFICATION/ FILTRATION |  |  |  |  |  |  |  |
| A1 - Cooling | Chemical - Coolant leak | PP – Equipment (BAC C1.2) |  |  |  |  |  |
| A2 - Buffer tank | None identified |  |  |  |  |  |  |
| A3 - Centrifuge | None identified |  |  |  |  |  |  |
| A4 - Buffer tank | None identified |  |  |  |  |  |  |
| A5 - Cooling tank | Chemical - Coolant leak | PP – Equipment (BAC C1.2) |  |  |  |  |  |
| A6 - Aging Tank | Chemical - Coolant leak | PP – Equipment (BAC C1.2) |  |  |  |  |  |
| A7 - Secondary Storage | Chemical - Coolant leak Sulphites as an allergen | PP – Equipment (BAC C1.2) Allergen Management Program |  |  |  |  |  |
| A8 - Surge/ buffer Tank | Chemical - Sulphites as an allergen | Allergen Management Program |  |  |  |  |  |
| A9 – Filtration | Chemical - Sulphites as an allergen | Allergen Management Program |  |  |  |  |  |
| A10 – Bright Beer Storage | (See PS6 below) |  |  |  |  |  |  |
| PS6 – BRIGHT BEER STORAGE | Chemical – Coolant leak Sulphites as an allergen Cleaning chemicals | PP – Equipment (BAC C1.2) Allergen Management Program PP - Sanitation (BAC E1.1) |  |  |  |  |  |
| PS7 BRIGHT BEER PROCESSING |  |  |  |  |  |  |  |
| PS7 (SF) – Sterile Filtration |  |  |  |  |  |  |  |
| SF1 - Bright Beer Tank | Chemical – Coolant leak Sulphites as an allergen Cleaning chemicals | PP – Equipment (BAC C1.2) Allergen Management Program PP - Sanitation (BAC E1.1) |  |  |  |  |  |
| SF2 - Filtration | Sulphites as an allergen | Allergen Management Program |  |  |  |  |  |
| SF3 - Sterile Beer Tank | None identified |  |  |  |  |  |  |
| PS7(FP) – Flash Pasteurization |  |  |  |  |  |  |  |
| FP1 - Bright Beer Tank | Chemical – Coolant leak Sulphites as an allergen Cleaning chemicals | PP – Equipment (BAC C1.2) Allergen Management Program PP - Sanitation (BAC E1.1) |  |  |  |  |  |
| FP2 - Pasteurization | Chemical – Contamination from coolant | PP – Equipment (BAC C1.2) |  |  |  |  |  |
| FP3 - Pasteurized Beer Tank | None identified |  |  |  |  |  |  |
| PS8 RB – Returned Bottles Prep (Float Glassware Prep) |  |  |  |  |  |  |  |
| RB1 - Receiving/ Storage | Physical - Damage to bottles | PP – Transportation, Receiving & Storage (BAC B1.1) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| RB2 - De-palletizing | Physical - Damage to bottles | PP – Equipment (BAC C1.2) PP – Transportation, Receiving & Storage (BAC B1.1) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| RB3- RB4 - De-casing & Inspection (visual) | Physical - Damage to bottles | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| RB5 - Bottle Wash Loading | Physical - Damage to bottles | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| RB6 - Pre-rinse sprays | Physical - Damage to bottles (e.g. Temperature shock due to storage) | PP – Equipment (BAC C1.2) PP – Transportation, Receiving & Storage (BAC B1.1) |  |  |  |  |  |
| RB7 - Soak Tanks With Caustic | Physical - Damage to bottles Chemical – Too concentrated, too low, no caustic, wrong chemical Chemical - Bottle unable to drain | PP – Equipment (BAC C1.2) PP – Equipment (BAC C1.2) PP – Transportation, Receiving & Storage (BAC B1.1) PP – Personnel (BAC D1.2) Training No | Yes (EBI/ RLD) | Yes | No | Yes(EBI/RLD) |  |
| RB8 - Hydro Jet Sprays | Biological – Spray malfunction and debris is left in bottle (e.g. pathogenic Clostridium, Listeria, Hepatitis (A/B/C) Physical - Damage to bottles, Physical - Bottle contains foreign object (spray malfunction) Physical – Bottle contains foreign object (plugged but sprays cannot clear object) Chemical – Bottle unable to drain | (Partially Controlled) PP – Equipment (BAC C1.2) (Partially Controlled) PP – Equipment (BAC C1.2) PP – Equipment (BAC C1.2) No No | Yes – (no pathogens known to survive in final product – properties of beer, e.g. low pH, alcohol content see Form 1) Yes (EBI) Yes (EBI) Yes (EBI/ RLD) | No Yes Yes Yes | No No No | Yes (EBI) Yes (EBI) Yes (EBI/ RLD) |  |
| RB9- Post-Soak | Physical - Damage to bottles (e.g. Temperature shock), Physical - Bottle plugged Chemical – Bottle unable to drain | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training No No | Yes (EBI) Yes (EBI) Yes (EBI/ RLD) | Yes Yes Yes | No No No | Yes (EBI) Yes (EBI) Yes (EBI/ RLD) |  |
| RB10 - External Flush | Physical - Damage to bottles (e.g. Temperature shock) | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training | Yes (EBI) | Yes | No | Yes (EBI) |  |
| RB11 - Ext. Rinse | Physical - Damage to bottles (e.g. Temperature shock) | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training | Yes (EBI) | Yes | No | Yes (EBI) |  |
| RB12 - Interior Rinse | Physical - Damage to bottles Physical - Bottle contains foreign object (spray malfunction) Physical – Bottle contains foreign object (plugged but sprays cannot clear object) Chemical – Spray malfunction Chemical - Bottle plugged unable to drain | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Equipment (BAC C1.2) No PP – Equipment (BAC C1.2) No | Yes (EBI) Yes (EBI) Yes (EBI/ RLD) | Yes Yes Yes | No No No | Yes (EBI) Yes (EBI) Yes (EBI/ RLD) |  |
| RB13 - Final Rinse | Physical - Damage to bottles, Physical - Bottle contains foreign object (spray malfunction) Physical – Bottle contains foreign object (plugged but sprays cannot clear object) Chemical – Bottle unable to drain | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Equipment (BAC C1.2) No No | Yes (EBI) Yes (EBI) Yes (EBI/ RLD) | Yes Yes Yes | No No No | Yes (EBI) Yes (EBI) Yes (EBI/ RLD) |  |
| PS8 NB - New Bottles (Glassware) Prep |  |  |  |  |  |  |  |
| NB1- NB2 - Receiving & Preliminary Inspection | Physical - Damage to bottles | PP – Transportation, Receiving & Storage (BAC B1.1) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| NB3 – NB 6 Storage (Pallet Prep, De-palletize) | Physical - Damage to bottles | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| NB7 – Inspection (Human, visual) | Physical – Missed critical glass defects | (Partially Controlled) PP – Personnel (BAC D1.2) Training | Yes (EBI) | Yes | No | Yes (EBI) |  |
| NB8 - Bottle Loading, | Physical – Damage to bottles | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| NB9 - Bulk Glass Rinser | Physical – Spray malfunction (e.g. plugged sprays) Chemical – Contaminated air, sanitizing spray | PP – Equipment (BAC C1.2) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| PS8 BT - BOTTLING |  |  |  |  |  |  |  |
| BT1 Empty Bottle Inspection Human or Machine inspection (EBI/ RLD) | MACHINE: Physical - Failure of the system to detect foreign matter, glass defects, bottle damage Chemical - Failure of the system to detect residual liquid and caustic HUMAN: Physical - Failure of personnel to detect foreign matter, glass defects, glass damage Chemical - Failure of personnel to detect residual liquid | MACHINE: (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training HUMAN: (Partially Controlled) PP – Personnel (BAC D1.2) Training, SOP (personnel rotation) (Partially Controlled) PP – Personnel (BAC D1.2) Training , SOP (personnel rotation) | Yes (EBI) Yes (EBI/ RLD) Yes (EBI) Yes (EBI | Yes Yes Yes Yes | Yes Yes Yes Yes |  | CCP1-P CCP1-C CCP1-P CCP1-C |
| BT2 – Down Bottle Filler In-Feed Control | Physical – Glass inclusions from breakage of down bottle at filler in-feed | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) |  |  |  |  |  |
| BT3 – BT5 Filling (Purges , Filling, Fobbing) | Physical – Chipping of bottles (e.g. from filling equipment), glass inclusion Auto-Flush: Physical – Burst bottle leading to glass inclusion Manual Flush: Physical – Burst bottle leading to glass inclusion | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training Auto-Flush: (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training PP – Transportation, Receiving & Storage (BAC B1.1) Manual Flush: | Yes (SOP Burst Bottle Detection System/ Filler Flush/ Auto Flush) Yes (SOP on Burst Bottle Monitoring and Reject & Flush) | Yes | Yes |  | CCP2-P |
| BT3 – BT5 Filling (Purges , Filling, Fobbing) (Continued) | Chemical – CIP chemicals in bottle | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training PP – Transportation, Receiving & Storage (BAC B1.1) PP - Sanitation (BAC E1.1) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |  | Yes | No | Yes (Foam Inspection&/or Candling) |  |
| BT6 - Crowning | Physical – Bottle finish damage (leading to glass inclusions) Chemical – Lubricants | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training PP – Equipment (BAC C1.2) | Yes (SOP, Foam Inspection &/or Candling) | Yes | No | Yes (Foam Inspection &/or Candling) |  |
| BT7 – BT 8 Bottle Flush (Full Bottle Wash - external) | None identified |  |  |  |  |  |  |
| BT9 – Pasteurize | None identified |  |  |  |  |  |  |
| BT10 - Foam Inspection &/or Candling (Human) Note: Automated Foam Inspection is not within the scope of this generic model. | Physical – Failure to detect foreign matter (including glass) | PP – Personnel (BAC D1.2) Training | Yes (increase number of inspectors) | No |  |  |  |
| BT11 – Drying (Bottle Drying and Air Knives) | None identified |  |  |  |  |  |  |
| BT12 – BT13 Labelling, Coding | Product not coded or not correctly coded | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) |  |  |  |  |  |
| BT14 – Filled Bottle Inspection | None identified |  |  |  |  |  |  |
| BT15 – BT18 Packing & Sealing (Divert to packers, Carton, Case Pack, Sealing) | None identified |  |  |  |  |  |  |
| BT19 – BT20 Secondary Code & Inspection (Secondary Packaging, Code/Inspection) | Product not coded, or not correctly coded | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) |  |  |  |  |  |
| BT21 – Palletize | None identified |  |  |  |  |  |  |
| BT22 - Storage (or Live Load) | None identified |  |  |  |  |  |  |
| BT23 - Shipping | None identified |  |  |  |  |  |  |
| PS8 (K) - KEGGING |  |  |  |  |  |  |  |
| K1 - Receiving (See PS1) | None identified |  |  |  |  |  |  |
| K2 – K3 Storage & Handling , De-palletizing (See PS2) | None identified |  |  |  |  |  |  |
| K4 - External Inspection | None identified |  |  |  |  |  |  |
| K5 – K6 External Cleaning (Ext Wash/Inspection) | Old codes not effectively removed | PP - Recall (BAC F1.2) |  |  |  |  |  |
| K7 – Racking | None identified |  |  |  |  |  |  |
| K8 – K12 Internal Cleaning (Purge, Flush, Wash, Purge, Rinse) | Automated Chemical – Cleaning solution not effectively removed. Manual: Chemical – Cleaning solution not effectively removed. | Automated PP - Sanitation (BAC E1.1) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training Manual: (Partially Controlled) PP - Sanitation (BAC E1.1) PP – Personnel (BAC D1.2) Training | No | Yes | Yes | Yes | CCP3-C |
| K13 - Sterilize & Hold | None identified |  |  |  |  |  |  |
| K14 – K 15 Purge to Empty & Counter pressure | None identified |  |  |  |  |  |  |
| K 16 - K17 Barnes Neck Sanitize & Inspect |  |  |  |  |  |  |  |
| K18 - Filling | Chemical – CIP solution | PP - Sanitation (BAC E1.1) PP – Personnel (BAC D1.2) Training PP – Equipment (BAC C1.2) |  |  |  |  |  |
| K19 – K 21 Barnes Neck, Wash & Sanitize | None identified |  |  |  |  |  |  |
| K22 - Dust Cap | None identified |  |  |  |  |  |  |
| K23 - Air Dry | None identified |  |  |  |  |  |  |
| K24 - Product Code Applied | Incorrect or missing code | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| K25 – K 26 Weigh (In-line weighing) & Palletize | None identified |  |  |  |  |  |  |
| K27 - Storage | None identified |  |  |  |  |  |  |
| K28 - Shipping | None identified |  |  |  |  |  |  |
| PS8 (C) - CANNING |  |  |  |  |  |  |  |
| C1 - Receiving | None identified |  |  |  |  |  |  |
| C2 - Storage & Handling | Biological – Bacterial contamination from leaking roof or pipes Chemical - Contamination from leaking roof or pipes | PP – Premises (BAC A1.1 & BAC A2.1) PP – Premises (BAC A1.1 & BAC A2.1) |  |  |  |  |  |
| C3 – C 4 De-palletize / Pallet ID (Collect & Timestamp Can Pallet ID, De-palletize) | Incorrect or missing code on pallet | PP - Recall (BAC F1.2) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| C5 - Online visual inspection | None identified |  |  |  |  |  |  |
| C6 - Primary code applied | Incorrect or missing code – | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| C7 - Bulk in-line rinser | Chemical – Chemicals from compressed air or water | PP – Premises (BAC A4.1) PP – Equipment (BAC C1.2) |  |  |  |  |  |
| C8 – C 10 Filling (pre-evacuation & beer fill) | None identified |  |  |  |  |  |  |
| C11 – C13 Seaming | Chemical – Chemicals, Lubricants | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| C14 - External Can Flush | None identified |  |  |  |  |  |  |
| C15 – Pasteurizer | None identified |  |  |  |  |  |  |
| C16 – C17 Drying | None identified |  |  |  |  |  |  |
| C18 - Fill Height Inspection | None identified |  |  |  |  |  |  |
| C19 - Divert to Packers | None identified |  |  |  |  |  |  |
| C20 - Hi-Cone Machine | None identified |  |  |  |  |  |  |
| C21 - Case Packers | None identified |  |  |  |  |  |  |
| C22 – Inspection (Human, visual) Inspection | None identified |  |  |  |  |  |  |
| C23 – C24 Tray Machine & Code | Incorrect or missing code | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| C25 – Palletize | None identified |  |  |  |  |  |  |
| C26 - Storage (or Live Load) | None identified |  |  |  |  |  |  |
| C27 – Shipping | None identified |  |  |  |  |  |  |
| PS8 T - TANKERING |  |  |  |  |  |  |  |
| T1 - Empty Tanker (Receiving) | Chemical – Cleaning chemicals and/ or sanitizer | PP – Transportation, Receiving & Storage (BAC B1.1) COA, Wash Ticket, PP – Personnel (BAC D1.2) Training |  |  |  |  |  |
| T2 - Tanker Washing/ Rinsing | Chemical – Cleaning chemicals and/ or sanitizer | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training PP - Sanitation (BAC E1.1) |  |  |  |  |  |
| T3 - Tanker Purging | Chemical – Contaminated CO2 | For Regenerated CO2 – PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training For Purchased CO2 - PP – Transportation, Receiving & Storage (BAC B1.1) COA |  |  |  |  |  |
| T4 - Tanker Filling/ Loading | Biological – Insect or pest infestation of hoses Chemical – Cross contamination from using hose on non-food material | No PP – Personnel (BAC D1.2) Training | Yes – (no pathogens known to survive in final product due to the properties of beer, e.g. low pH, see Form 1) | No |  |  |  |
| T5 – Tanker Shipping | None identified |  |  |  |  |  |  |
| T6 – T7 Full Tanker Receiving & Unloading | Biological – Insect or pest infestation of hoses Chemical – Cross contamination with chemicals from the supplier Chemical – Cross contamination from using hose on non-food material | No PP – Transportation, Receiving & Storage (BAC B1.1) + COA PP – Personnel (BAC D1.2) Training | Yes – (no pathogens known to survive in final product due to the properties of beer, e.g. low pH, alcohol content see Form 1) | No |  |  |  |

| Date: | Approved by: |
| --- | --- |

# Form 3a:

# Process Flow Diagram with ccps

Date: _______________ Approved by: ________________________________

# Form 5a:

# biological hazards control & ccps

| BAC Generic | Title: Form 5A – Hazard Identification - Biological Hazards Control & CCPs |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

Note – No CCPs were identified for biological hazards in Beer.

| List all biological hazards related to ingredients, incoming material, processing, product flow, etc. | Identified biological hazards (Bacteria, parasites, viruses, etc.) | Controlled at: |
| --- | --- | --- |
| INGREDIENTS |
| LIQUID INGREDIENTS |  |  |
| City Water | Coliform, E. Coli | PP – Premises, Water Quality (BAC A4.1) |
| Purchased Water | Coliform, E. Coli | PP – Premises, Water Quality (BAC A4.1) |
| Well/ Lake/ Surface/ Water | Coliform, E. Coli, Parasites | PP – Premises, Water Quality (BAC A4.1) |
| DRY INGREDIENTS |  |  |
| Barley malt | Micro (fecal contamination from birds, mice) | PP - Transportation Receiving & Storage (BAC B1.1) - COA from supplier |
| Wheat (malted/ non-malted), | Micro (fecal contamination from birds, mice) | PP - Transportation Receiving & Storage (BAC B1.1) + COA from supplier |
| Cereal Grain, e.g. corn, oats, rice | Micro (fecal contamination from birds, mice) | PP - Transportation Receiving & Storage (BAC B1.1) + COA from supplier |
| Hops | Fecal contamination (E. coli) | PP - Transportation Receiving & Storage (BAC B1.1) + COA |
| OTHER INGREDIENTS |  |  |
| Yeast | Cross contaminated e.g. Salmonella | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Carbohydrate Matter (e.g. sucrose, syrup, honey) | Clostridium | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Salt | None identified |  |
| Hop Oil | None identified | + PP – Transportation, Receiving & Storage (BAC B1.1) +COA |
| Hop Extract | None identified |  |
| Nitrogen/ Oxygen/ Compressed Air Purchased CO2 | None Identified |  |
| Regenerated CO2 | None identified |  |
| Liquid Wheat Extract | None identified |  |
| Caramel | None identified |  |
| Dextrin | None Identified |  |
| Food Enzymes | None identified |  |
| Stabilizing Agents | None identified |  |
| Water preparation agents | None identified |  |
| Preservatives | None Identified |  |
| Yeast Foods | None Identified |  |
| Processing aids Examples – Gelatin, Irish Moss, Wood Shavings | Fecal contamination (e.g. Gelatin, Irish Moss) | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| PRIMARY PACKAGING MATERIAL |
| New glass | None identified |  |
| Used glass | Bacteria | No pathogens known to survive in final product due to properties of beer, e.g. low pH, alcohol content see Form 1 |
| Lined aluminum cans and bottles | None identified |  |
| New Kegs | None identified |  |
| Used Kegs | None identified |  |
| Plastic Bottles, e.g. PET | None Identified |  |
| Crowns | None identified |  |
| Closures & Can Ends | None Identified |  |
| PROCESS STEPS |
| PS1- RECEIVING | Micro contamination from receiving open containers (e.g. bird droppings). | PP – Premises (BAC A1.1 & BAC A2.1) PP - Pest Control (BAC E2.1) |
| PS2- STORAGE/ HANDLING | Mold growth from improper storage conditions Insect or pest infestation | PP - Premises (BAC A2.1) PP - Sanitation (BAC E1.1) PP - Pest Control (BAC E2.1) |
| PS3 - Brewing |  |  |
| B1 - Receiving | (See PS1 above) |  |
| B2 - Storage | (See PS2 above) |  |
| B3 - Milling | None identified |  |
| B4 - Cereal Cooker | None identified |  |
| B5 - Mashing (Mash Mixer, Mash Cooker) | None identified |  |
| B6 - Lautering (Lauter Tun, Mash Filter removal of spent grains | None identified |  |
| PROCESS STEPS (Continued) |
| B7 – Holding Tank | None identified |  |
| B8 - Kettle | None identified |  |
| B9 Whirlpool | None identified |  |
| B10 - Wort Cooling (Heat Exchanger) | None identified |  |
| PS4 -Fermentation |  |  |
| Cold Wort (from B10) | None identified |  |
| F1 Wort Oxygenation/ Wort Aeration | None identified |  |
| F2 - Fermentation | None identified |  |
| F3 - Cooling | None identified |  |
| F4 - Green Beer | None identified |  |
| PS4 – Sub-Process Yeast Preparation |  |  |
| Y1 – Propagation | None identified |  |
| Y2 – Storage | None identified |  |
| Y3 – Acid Washing | None identified |  |
| PS5 - AGING/ CLARIFICATION/ FILTRATION |  |  |
| A1 - Cooling | None identified |  |
| A2 - Buffer tank | None identified |  |
| A3 - Centrifuge | None identified |  |
| A4 - Buffer tank | None identified |  |
| A5 - Cooling tank | None identified |  |
| A6 - Aging Tank | None identified |  |
| A7 - Secondary Storage | None identified |  |
| PROCESS STEPS (Continued) |
| A8 - Surge/ buffer Tank | None identified |  |
| A9 – Filtration | None identified |  |
| A10 – Bright Beer Storage | (See PS6 below) |  |
| PS6 – BRIGHT BEER STORAGE | None identified |  |
| PS7 BRIGHT BEER PROCESSING |  |  |
| PS7 (SF) – Sterile Filtration |  |  |
| SF1 - Bright Beer Tank | None identified |  |
| SF2 - Filtration | None identified |  |
| SF3 - Sterile Beer Tank | None identified |  |
| PS7(FP) – Flash Pasteurization |  |  |
| FP1 - Bright Beer Tank | None identified |  |
| FP2 - Pasteurization | None identified |  |
| FP3 - Pasteurized Beer Tank | None identified |  |
| PS8 RB – Returned Bottles Prep (Float Glassware Prep) |  |  |
| RB1 - Receiving/ Storage | None identified |  |
| RB2 - De-palletizing | None identified |  |
| RB3- RB4 - De-casing & Inspection (visual) | None identified |  |
| RB5 - Bottle Wash Loading | None identified |  |
| RB6 - Pre-rinse sprays | None identified |  |
| RB7 - Soak Tanks With Caustic | None identified |  |
| RB8 - Hydro Jet Sprays | Spray malfunction and debris is left in bottle (e.g. pathogenic Clostridium, Listeria, Hepatitis (A/B/C) | (Partially Controlled) PP – Equipment (BAC C1.2) Also, no pathogens known to survive in final product – properties of beer, e.g. low pH, alcohol content see Form 1. |
| PROCESS STEPS (Continued) |
| RB9- Post-Soak | None identified |  |
| RB10 - External Flush | None identified |  |
| RB11 - Ext. Rinse | None identified |  |
| RB12 - Interior Rinse | None identified |  |
| RB13 - Final Rinse | None identified |  |
| PS8 NB - New Bottles (Glassware) Prep |  |  |
| NB1- NB2 - Receiving & Preliminary Inspection | None identified |  |
| NB3 – NB 6 Storage (Pallet Prep, De-palletize) | None identified |  |
| NB7 – Inspection (Human, visual) | None identified |  |
| NB8 - Bottle Loading, | None identified |  |
| NB9 - Bulk Glass Rinser | None identified |  |
| PS8 BT - BOTTLING |  |  |
| BT1 Empty Bottle Inspection (Human or Machine inspection) | None identified |  |
| BT2 – Down Bottle Filler In-Feed Control | None identified |  |
| BT3 – BT5 Filling (Purges , Filling, Fobbing) | None identified |  |
| BT6 - Crowning | None identified |  |
| BT7 – BT 8 Bottle Flush (Full Bottle Wash - external) | None identified |  |
| BT9 – Pasteurize | None identified |  |
| BT10 - Foam Inspection &/or Candling | None identified |  |
| PROCESS STEPS (Continued) |
| BT11 – Drying (Bottle Drying and Air Knives) | None identified |  |
| BT12 – BT13 Labelling, Coding | None identified |  |
| BT14 – Filled Bottle Inspection | None identified |  |
| BT15 – BT18 Packing & Sealing (Divert to packers, Carton, Case Pack, Sealing) | None identified |  |
| BT19 – BT20 Secondary Code & Inspection (Secondary Packaging, Code/Inspection) | None identified |  |
| BT21 – Palletize | None identified |  |
| BT22 - Storage (or Live Load) | None identified |  |
| BT23 - Shipping | None identified |  |
| PS8 (K) - KEGGING |  |  |
| K1 - Receiving (See PS1) | None identified |  |
| K2 – K3 Storage & Handling , De-palletizing (See PS2) | None identified |  |
| K4 - External Inspection | None identified |  |
| K5 – K6 External Cleaning (Ext Wash/Inspection) | None identified |  |
| K7 – Racking | None identified |  |
| K8 – K12 Internal Cleaning (Purge, Flush, Wash, Purge, Rinse) | None identified |  |
| K13 - Sterilize & Hold | None identified |  |
| K14 – K 15 Purge to Empty & Counter pressure | None identified |  |
| K 16 - K17 Barnes Neck Sanitize & Inspect | None identified |  |
| PROCESS STEPS (Continued) |
| K18 - Filling | None identified |  |
| K19 – K 21 Barnes Neck, Wash & Sanitize | None identified |  |
| K22 - Dust Cap | None identified |  |
| K23 - Air Dry | None identified |  |
| K24 - Product Code Applied | None identified |  |
| K25 – K 26 Weigh (In-line weighing) & Palletize | None identified |  |
| K27 - Storage | None identified |  |
| K28 - Shipping | None identified |  |
| PS8 (C) - CANNING |  |  |
| C1 - Receiving | None identified |  |
| C2 - Storage & Handling | Bacterial contamination from leaking roof or pipes | PP – Premises (BAC A1.1 & BAC A2.1) |
| C3 – C 4 De-palletize / Pallet ID (Collect & Timestamp Can Pallet ID, De-palletize) | None identified |  |
| C5 - Online visual inspection | None identified |  |
| C6 - Primary code applied | None identified |  |
| C7 - Bulk in-line rinser | None identified |  |
| C8 – C 10 Filling (pre-evacuation & beer fill) | None identified |  |
| C11 – C13 Seaming | None identified |  |
| C14 - External Can Flush | None identified |  |
| C15 – Pasteurizer | None identified |  |
| C16 – C17 Drying | None identified |  |
| C18 - Fill Height Inspection | None identified |  |
| PROCESS STEPS (Continued) |
| C19 - Divert to Packers | None identified |  |
| C20 - Hi-Cone Machine | None identified |  |
| C21 - Case Packers | None identified |  |
| C22 – Inspection (Human, visual) Inspection | None identified |  |
| C23 – C24 Tray Machine & Code | None identified |  |
| C25 – Palletize | None identified |  |
| C26 - Storage (or Live Load) | None identified |  |
| C27 – Shipping | None identified |  |
| PS8 T - TANKERING |  |  |
| T1 - Empty Tanker (Receiving) | None identified |  |
| T2 - Tanker Washing/ Rinsing | None identified |  |
| T3 - Tanker Purging | None identified |  |
| T4 - Tanker Filling/ Loading | Insect or pest infestation of hoses | No pathogens known to survive in final product due to properties of beer, e.g. low pH, alcohol content see Form 1 |
| T5 – Tanker Shipping | None identified |  |
| T6 – T7 Full Tanker Receiving & Unloading | Insect or pest infestation of hoses | No pathogens known to survive in final product due to properties of beer, e.g. low pH, alcohol content see Form 1 |

| Date: | Approved by: |
| --- | --- |

# Form 6a:

# chemical hazards control & ccps

| BAC Generic | Title: Form 6A Hazard Identification - Chemical Hazards Control & CCPs |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

| List all chemical hazards related to ingredients, incoming material, processing, product flow, etc. | Identified chemical hazards | Controlled at: |
| --- | --- | --- |
| INGREDIENTS |
| LIQUID INGREDIENTS |  |
| City Water | Pesticides, Heavy metals | PP – Premises, Water Quality (BAC A4.1) |
| Purchased Water | Cleaning chemicals, cross contamination from previous load | PP - Transportation Receiving & Storage (BAC B1.1) - COA/ Supplier Audits |
| Well/ Lake/ Surface/ Water | Pesticides, Heavy metals | PP – Premises, Water Quality (BAC A4.1) |
| DRY INGREDIENTS |  |
| Barley malt | Pesticides, Mycotoxins, Allergen (cross-contamination from carrier), NDMA | PP - Transportation Receiving & Storage (BAC B1.1)- COA / Letter of Guarantee |
| Wheat (malted/ non-malted), | Pesticides, Mycotoxins, Allergen, NDMA | PP - Transportation Receiving & Storage (BAC B1.1) + COA / Letter of Guarantee, Allergen Management Program |
| Cereal Grain, e.g. corn, oats, rice | Pesticides, Mycotoxins, Allergen (cross-contamination from carrier), NDMA | PP - Transportation Receiving & Storage (BAC B1.1) + COA / Letter of Guarantee, Allergen Management Program |
| Hops | Pesticides, Mycotoxins | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| OTHER INGREDIENTS (Continued) |  |
| Yeast | Heavy Metals, cleaning chemicals (used in tankers) | PP – Transportation, Receiving & Storage (BAC B1.1) + COA, Wash Tickets |
| Carbohydrate Matter (e.g. sucrose, syrup, honey) | Antibiotic residue, heavy metal (honey) | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Salt | Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Hop Oil | Residual solvents, Non-food grade | + PP – Transportation, Receiving & Storage (BAC B1.1) COA |
| Hop Extract | Residual solvents, Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Nitrogen/ Oxygen/ Compressed Air Purchased CO2 | Chemical non-volatile gases, Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA, QC Testing |
| Regenerated CO2 | Contamination from oil (from the compressor) | PP - Equipment (BAC C1.2) |
| Liquid Wheat Extract | Allergen | Allergen Management Program |
| Caramel | Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Dextrin | Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Food Enzymes | Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| OTHER INGREDIENTS (Continued) |  |
| Stabilizing Agents | Heavy metals, Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Water preparation agents | Heavy metals, Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Preservatives | Allergens (Sulphites), Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA, Allergen Management Program |
| Yeast Foods | Heavy metals, Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Processing aids Examples – Gelatin, Irish Moss, Wood Shavings | Heavy metals, Non-food grade | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| PRIMARY PACKAGING MATERIAL |
| New glass | None identified |  |
| Used glass | Lubricants, mycotoxins | PP – Transportation, Receiving & Storage (BAC B1.1) (Partially Controlled) + Inspection, + EBI (Empty Bottle Inspection) / RLD(Residual Liquid Detector) |
| Lined aluminum cans and bottles | None identified |  |
| New Kegs | None identified |  |
| Used Kegs | None identified |  |
| Plastic Bottles, e.g. PET | None identified |  |
| PRIMARY PACKAGING MATERIAL (Continued) |
| Crowns | None identified |  |
| Closures & Can Ends | None identified |  |
| PROCESS STEPS |
| PS1- RECEIVING | Chemical – Contamination from truck (damage, leaks, odors) | PP – Transportation, Receiving & Storage (BAC B1.1) |
| PS2- STORAGE/ HANDLING | Chemical - Cross-contamination from allergens (e.g. wheat) | Allergen Management Program |
| PS3 - Brewing |  |  |
| B1 - Receiving | (See PS1 above) |  |
| B2 - Storage | (See PS2 above) |  |
| B3 - Milling | Chemical – Allergen cross-contamination (e.g. from residues in the mill) | PP - Sanitation (BAC E1.1) Allergen Management Program |
| B4 - Cereal Cooker | None identified |  |
| B5 - Mashing (Mash Mixer, Mash Cooker) | None identified |  |
| B6 - Lautering (Lauter Tun, Mash Filter removal of spent grains | None identified |  |
| B7 – Holding Tank | None identified |  |
| B8 - Kettle | None identified |  |
| B9 Whirlpool | None identified |  |
| B10 - Wort Cooling (Heat Exchanger) | None identified |  |
| PS4 -Fermentation |  |  |
| Cold Wort (from B10) | None identified |  |
| F1 Wort Oxygenation/ Wort Aeration | None identified |  |
| PROCESS STEPS |
| F2 - Fermentation | None identified |  |
| F3 - Cooling | Coolant leak | PP – Equipment (BAC C1.2) |
| F4 - Green Beer | None identified |  |
| PS4 – Sub-Process Yeast Preparation |  |  |
| Y1 – Propagation | None identified |  |
| Y2 – Storage | None identified |  |
| Y3 – Acid Washing | None identified |  |
| PS5 - AGING/ CLARIFICATION/ FILTRATION |  |  |
| A1 - Cooling | Coolant leak | PP – Equipment (BAC C1.2) |
| A2 - Buffer tank | None identified |  |
| A3 - Centrifuge | None identified |  |
| A4 - Buffer tank | None identified |  |
| A5 - Cooling tank | Coolant leak | PP – Equipment (BAC C1.2) |
| A6 - Aging Tank | Coolant leak | PP – Equipment (BAC C1.2) |
| A7 - Secondary Storage | Coolant leak Sulphites as an allergen | PP – Equipment (BAC C1.2) Allergen Management Program |
| A8 - Surge/ buffer Tank | Sulphites as an allergen | Allergen Management Program |
| A9 – Filtration | Sulphites as an allergen | Allergen Management Program |
| A10 – Bright Beer Storage | (See PS6 below) |  |
| PS6 – BRIGHT BEER STORAGE | Coolant leak Sulphites as an allergen Cleaning chemicals | PP – Equipment (BAC C1.2) Allergen Management Program PP - Sanitation (BAC E1.1) |
| PS7 BRIGHT BEER PROCESSING |  |  |
| PROCESS STEPS (Continued) |
| PS7 (SF) – Sterile Filtration |  |  |
| SF1 - Bright Beer Tank | Coolant leak Sulphites as an allergen Cleaning chemicals | PP – Equipment (BAC C1.2) Allergen Management Program PP - Sanitation (BAC E1.1) |
| SF2 - Filtration | Sulphites as an allergen | Allergen Management Program |
| SF3 - Sterile Beer Tank | None identified |  |
| PS7(FP) – Flash Pasteurization |  |  |
| FP1 - Bright Beer Tank | Coolant leak Sulphites as an allergen Cleaning chemicals | PP – Equipment (BAC C1.2) Allergen Management Program PP - Sanitation (BAC E1.1) |
| FP2 - Pasteurization | Contamination from coolant | PP – Equipment (BAC C1.2) |
| FP3 - Pasteurized Beer Tank | None identified |  |
| PS8 RB – Returned Bottles Prep (Float Glassware Prep) |  |  |
| RB1 - Receiving/ Storage | None identified |  |
| RB2 - De-palletizing | None identified |  |
| RB3- RB4 - De-casing & Inspection (visual) | None identified |  |
| RB5 - Bottle Wash Loading | None identified |  |
| RB6 - Pre-rinse sprays | None identified |  |
| RB7 - Soak Tanks With Caustic | Too concentrated, too low, no caustic, wrong chemical Bottle unable to drain | PP – Equipment (BAC C1.2) PP – Transportation, Receiving & Storage (BAC B1.1) PP – Personnel (BAC D1.2) Training |
| PROCESS STEPS (Continued) |
| RB8 - Hydro Jet Sprays | Bottle unable to drain | EBI (Empty Bottle Inspection)/RLD(Residual Liquid Detector) |
| RB9- Post-Soak | Bottle unable to drain | EBI/RLD |
| RB10 - External Flush | None identified |  |
| RB11 - Ext. Rinse | None identified |  |
| RB12 - Interior Rinse | Spray malfunction Bottle plugged unable to drain | PP – Equipment (BAC C1.2) EBI/ RLD |
| RB13 - Final Rinse | Bottle unable to drain | EBI/ RLD |
| PS8 NB - New Bottles (Glassware) Prep |  |  |
| NB1- NB2 - Receiving & Preliminary Inspection | None identified |  |
| NB3 – NB 6 Storage (Pallet Prep, De-palletize) | None identified |  |
| NB7 – Inspection (Human, visual) | None identified |  |
| NB8 - Bottle Loading, | None identified |  |
| NB9 - Bulk Glass Rinser | Contaminated air, sanitizing spray | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| PS8 BT - BOTTLING |  |  |
| BT1 Empty Bottle Inspection (Human or Machine inspection) | MACHINE: Failure of the system to detect residual liquid and caustic HUMAN: Failure of personnel to detect residual liquid | MACHINE: (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training CCP1-C HUMAN: (Partially Controlled) PP – Personnel (BAC D1.2) Training SOP (personnel rotation) CCP1-C |
| PROCESS STEPS (Continued) |
| BT2 – Down Bottle Filler In-Feed Control | None identified |  |
| BT3 – BT5 Filling (Purges , Filling, Fobbing) | CIP chemicals in bottle | PP - Sanitation (BAC E1.1) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| BT6 - Crowning | Lubricants | PP – Equipment (BAC C1.2) |
| BT7 – BT 8 Bottle Flush (Full Bottle Wash - external) | None identified |  |
| BT9 – Pasteurize | None identified |  |
| BT10 - Foam Inspection &/or Candling | None identified |  |
| BT11 – Drying (Bottle Drying and Air Knives) | None identified |  |
| BT12 – BT13 Labelling, Coding | Product not coded or not correctly coded | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) |
| BT14 – Filled Bottle Inspection | None identified |  |
| BT15 – BT18 Packing & Sealing (Divert to packers, Carton, Case Pack, Sealing) | None identified |  |
| BT19 – BT20 Secondary Code & Inspection (Secondary Packaging, Code/Inspection) | Product not coded or not correctly coded | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) |
| BT21 – Palletize | None identified |  |
| BT22 - Storage (or Live Load) | None identified |  |
| BT23 - Shipping | None identified |  |
| PROCESS STEPS (Continued) |
| PS8 (K) - KEGGING |  |  |
| K1 - Receiving (See PS1) | None identified |  |
| K2 – K3 Storage & Handling , De-palletizing (See PS2) | None identified |  |
| K4 - External Inspection | None identified |  |
| K5 – K6 External Cleaning (Ext Wash/Inspection) | Old codes not effectively removed | PP - Recall (BAC F1.2) |
| K7 – Racking | None identified |  |
| K8 – K12 Internal Cleaning (Purge, Flush, Wash, Purge, Rinse) | Automated Cleaning solution not effectively removed. Manual Cleaning solution not effectively removed. | Automated PP - Sanitation (BAC E1.1) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training Manual (Partially Controlled) PP - Sanitation (BAC E1.1) PP – Personnel (BAC D1.2) Training CCP3-C |
| K13 - Sterilize & Hold | None identified |  |
| K14 – K 15 Purge to Empty & Counter pressure | None identified |  |
| K 16 - K17 Barnes Neck Sanitize & Inspect | None identified |  |
| K18 - Filling | CIP solution | PP - Sanitation (BAC E1.1) PP – Personnel (BAC D1.2) Training PP – Equipment (BAC C1.2) |
| PROCESS STEPS (Continued) |
| K19 – K 21 Barnes Neck, Wash & Sanitize | None identified |  |
| K22 - Dust Cap | None identified |  |
| K23 - Air Dry | None identified |  |
| K24 - Product Code Applied | Incorrect or missing code | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| K25 – K 26 Weigh (In-line weighing) & Palletize | None identified |  |
| K27 - Storage | None identified |  |
| K28 - Shipping | None identified |  |
| PS8 (C) - CANNING |  |  |
| C1 - Receiving | None identified |  |
| C2 - Storage & Handling | Contamination from leaking roof or pipes | PP – Premises (BAC A1.1 & BAC A2.1) |
| C3 – C 4 De-palletize / Pallet ID (Collect & Timestamp Can Pallet ID, De-palletize) | Incorrect or missing code on pallet | PP - Recall (BAC F1.2) PP – Personnel (BAC D1.2) Training |
| C5 - Online visual inspection | None identified |  |
| C6 - Primary code applied | Incorrect or missing code – | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| C7 - Bulk in-line rinser | Chemicals from compressed air or water | PP – Premises (BAC A1.1 & BAC A2.1) PP – Equipment (BAC C1.2) |
| C8 – C 10 Filling (pre-evacuation & beer fill) | None identified |  |
| C11 – C13 Seaming | Chemicals, Lubricants | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| PROCESS STEPS (Continued) |
| C14 - External Can Flush | None identified |  |
| C15 – Pasteurizer | None identified |  |
| C16 – C17 Drying | None identified |  |
| C18 - Fill Height Inspection | None identified |  |
| C19 - Divert to Packers | None identified |  |
| C20 - Hi-Cone Machine | None identified |  |
| C21 - Case Packers | None identified |  |
| C22 – Inspection (Human, visual) Inspection | None identified |  |
| C23 – C24 Tray Machine & Code | Incorrect or missing code | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| C25 – Palletize | None identified |  |
| C26 – Storage (or Live Load) | None identified |  |
| C27 – Shipping | None identified |  |
| PS8 T - TANKERING |  |  |
| T1 - Empty Tanker (Receiving) | Cleaning chemicals and/ or sanitizer | PP – Transportation, Receiving & Storage (BAC B1.1) COA, Wash Ticket, PP – Personnel (BAC D1.2) Training |
| T2 - Tanker Washing/ Rinsing | Cleaning chemicals and/ or sanitizer | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training PP - Sanitation (BAC E1.1) |
| PROCESS STEPS (Continued) |
| T3 - Tanker Purging | Contaminated CO2 | For Regenerated CO2 – PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training For Purchased CO2 - PP – Transportation, Receiving & Storage (BAC B1.1) COA |
| T4 - Tanker Filling/ Loading | Cross contamination from using hose on non-food material | PP – Personnel (BAC D1.2) Training |
| T5 – Tanker Shipping | None identified |  |
| T6 – T7 Full Tanker Receiving & Unloading | Cross contamination with chemicals from the supplier Cross contamination from using hose on non-food material | PP – Transportation, Receiving & Storage (BAC B1.1) + COA PP – Personnel (BAC D1.2) Training |

| Date: | Approved by: |
| --- | --- |

# Form 7a:

# physical hazards controls & ccps

| BAC Generic | Title: Form 7A – Hazard Identification - Physical Hazards Control & CCPs |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

| List all physical hazards related to ingredients, incoming material, processing, product flow, etc. | Identified physical hazards | Controlled at: |
| --- | --- | --- |
| INGREDIENTS |
| LIQUID INGREDIENTS |  |  |
| City Water | Silt | PP – Premises, Water Quality (BAC A4.1) |
| Purchased Water | None identified |  |
| Well/ Lake/ Surface/ Water | Silt | PP – Premises, Water Quality (BAC A4.1) |
| DRY INGREDIENTS |  |  |
| Barley malt | Glass, Metal | PP - Transportation Receiving & Storage (BAC B1.1) - Receiving Inspection (screens, magnets) |
| Wheat (malted/ non-malted), | Glass, Metal | PP - Transportation Receiving & Storage (BAC B1.1) + Receiving Inspection (screens, magnets) |
| Cereal Grain, e.g. corn, oats, rice | Glass, Metal | PP - Transportation Receiving & Storage (BAC B1.1) + Receiving Inspection (screens, magnets) |
| Hops | Insects, metal | PP - Transportation Receiving & Storage (BAC B1.1) + COA, Inspection |
| OTHER INGREDIENTS |  |  |
| Yeast | None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA, Wash Tickets |
| Carbohydrate Matter (e.g. sucrose, syrup, honey) | None identified | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Salt | Rocks | (Partially Controlled) PP – Transportation, Receiving & Storage (BAC B1.1) + Inspection |
| Hop Oil | Plastic | PP – Transportation, Receiving & Storage (BAC B1.1) + COA, Inspection |
| Hop Extract | Plastic | PP – Transportation, Receiving & Storage (BAC B1.1) + COA, Inspection |
| Nitrogen/ Oxygen/ Compressed Air Purchased CO2 | None identified |  |
| Regenerated CO2 | None identified |  |
| Liquid Wheat Extract | Plastic (from packaging) | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Caramel | Plastic (from container) | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Dextrin | Plastic (from container) | PP – Transportation, Receiving & Storage (BAC B1.1) + COA |
| Food Enzymes | None identified |  |
| OTHER INGREDIENTS (Continued) |  |
| Stabilizing Agents | None identified |  |
| Water preparation agents | None identified |  |
| Preservatives | None identified |  |
| Yeast Foods | None identified |  |
| Processing aids Examples – Gelatin, Irish Moss, Wood Shavings | None identified |  |
| PRIMARY PACKAGING MATERIAL |
| New glass | Critical Glass Defects , Glass | (Partially Controlled) PP – Transportation, Receiving & Storage (BAC B1.1) +COA, Inspection + EBI (Empty Bottle Inspection) |
| Used glass | Critical Glass Defects , Dirt, Dust, Glass, Syringes, Medical Patches, | + Bottle Wash + EBI (Empty Bottle Inspection) |
| Lined aluminum cans and bottles | Metal Shavings | (Partially Controlled) PP – Transportation, Receiving & Storage (BAC B1.1) +COA + Rinse |
| New Kegs | Metal Shavings | (Partially Controlled) Rinse |
| Used Kegs | None identified |  |
| Plastic Bottles, e.g. PET | None identified |  |
| Crowns | None identified |  |
| Closures & Can Ends | None identified |  |

| PROCESS STEPS |
| --- |
| PS1- RECEIVING | Pests in hoses used for transferring material, Bulk Receiving | PP – Personnel (BAC D1.2) + Training |
| PS2- STORAGE/ HANDLING | Insect or pest infestation | PP - Pest Control (BAC E2.1) |
| PS3 - Brewing |  |  |
| B1 - Receiving | (See PS1 above) |  |
| B2 - Storage | (See PS2 above) |  |
| B3 - Milling | None identified |  |
| B4 - Cereal Cooker | None identified |  |
| B5 - Mashing (Mash Mixer, Mash Cooker) | None identified |  |
| B6 - Lautering (Lauter Tun, Mash Filter removal of spent grains | None identified |  |
| B7 – Holding Tank | None identified |  |
| B8 - Kettle | None identified |  |
| B9 Whirlpool | None identified |  |
| B10 - Wort Cooling (Heat Exchanger) | None identified |  |
| PS4 -Fermentation |  |  |
| Cold Wort (from B10) | None identified |  |
| F1 Wort Oxygenation/ Wort Aeration | None identified |  |
| F2 - Fermentation | None identified |  |
| F3 - Cooling |  |  |
| F4 - Green Beer | None identified |  |
| PS4 – Sub-Process Yeast Preparation |  |  |
| PROCESS STEPS (Continued) |
| Y1 – Propagation | None identified |  |
| Y2 – Storage | None identified |  |
| Y3 – Acid Washing | None identified |  |
| PS5 - AGING/ CLARIFICATION/ FILTRATION |  |  |
| A1 - Cooling |  |  |
| A2 - Buffer tank | None identified |  |
| A3 - Centrifuge | None identified |  |
| A4 - Buffer tank | None identified |  |
| A5 - Cooling tank | None identified |  |
| A6 - Aging Tank | None identified |  |
| A7 - Secondary Storage | None identified |  |
| A8 - Surge/ buffer Tank | None identified |  |
| A9 – Filtration | None identified |  |
| A10 – Bright Beer Storage | None identified |  |
| PS6 – BRIGHT BEER STORAGE | None identified |  |
| PS7 BRIGHT BEER PROCESSING |  |  |
| PS7 (SF) – Sterile Filtration |  |  |
| SF1 - Bright Beer Tank | None identified |  |
| SF2 - Filtration | None identified |  |
| SF3 - Sterile Beer Tank | None identified |  |
| PS7(FP) – Flash Pasteurization |  |  |
| FP1 - Bright Beer Tank | None identified |  |
| PROCESS STEPS (Continued) |
| FP2 - Pasteurization | None identified |  |
| FP3 - Pasteurized Beer Tank | None identified |  |
| PS8 RB – Returned Bottles Prep (Float Glassware Prep) |  |  |
| RB1 - Receiving/ Storage | Damage to bottles | PP – Transportation, Receiving & Storage (BAC B1.1) PP – Personnel (BAC D1.2) Training |
| RB2 - De-palletizing | Damage to bottles | PP – Equipment (BAC C1.2) PP – Transportation, Receiving & Storage (BAC B1.1) PP – Personnel (BAC D1.2) Training |
| RB3- RB4 - De-casing & Inspection (visual) | Damage to bottles | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| RB5 - Bottle Wash Loading | Damage to bottles | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| RB6 - Pre-rinse sprays | Damage to bottles (e.g. Temperature shock due to storage) | PP – Equipment (BAC C1.2) PP – Transportation, Receiving & Storage (BAC B1.1) |
| RB7 - Soak Tanks With Caustic | Damage to bottles | PP – Equipment (BAC C1.2) |
| RB8 - Hydro Jet Sprays | Damage to bottles, Bottle contains foreign object (spray malfunction) Bottle contains foreign object (plugged but sprays cannot clear object) | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Equipment (BAC C1.2) +EBI |
| RB9- Post-Soak | Damage to bottles (e.g. Temperature shock), Bottle plugged | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training +EBI |
| PROCESS STEPS (Continued) |
| RB10 - External Flush | Damage to bottles (e.g. Temperature shock) | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training +EBI |
| RB11 - Ext. Rinse | Damage to bottles (e.g. Temperature shock) | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training +EBI |
| RB12 - Interior Rinse | Damage to bottles Bottle contains foreign object (spray malfunction) Bottle contains foreign object (plugged but sprays cannot clear object) | PP – Equipment (BAC C1.2) PP – Equipment (BAC C1.2) +EBI |
| RB13 - Final Rinse | Damage to bottles, Bottle contains foreign object (spray malfunction) Bottle contains foreign object (plugged but sprays cannot clear object) | PP – Equipment (BAC C1.2) PP – Equipment (BAC C1.2) +EBI |
| PS8 NB - New Bottles (Glassware) Prep |  |  |
| NB1- NB2 - Receiving & Preliminary Inspection | Damage to bottles | PP – Transportation, Receiving & Storage (BAC B1.1) PP – Personnel (BAC D1.2) Training |
| NB3 – NB 6 Storage (Pallet Prep, De-palletize) | Damage to bottles | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| NB7 – Inspection (Human, visual) | Missed critical glass defects | (Partially Controlled) PP – Personnel (BAC D1.2) Training +EBI |
| PROCESS STEPS (Continued) |
| NB8 - Bottle Loading, | Damage to bottles | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| NB9 - Bulk Glass Rinser | Spray malfunction (e.g. plugged sprays) | PP – Equipment (BAC C1.2) |
| PS8 BT - BOTTLING |  |  |
| BT1 Empty Bottle Inspection (Human or Machine inspection) | MACHINE: Failure of the system to detect foreign matter, glass defects, bottle damage HUMAN: Failure of personnel to detect foreign matter, glass defects, glass damage | MACHINE: (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training CCP1-P HUMAN: (Partially Controlled) PP – Personnel (BAC D1.2) Training, SOP (personnel rotation) CCP1-P |
| BT2 – Down Bottle Filler In-Feed Control | Glass inclusions from breakage of down bottle at filler in-feed | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) |
| BT3 – BT5 Filling (Purges , Filling, Fobbing) | Chipping of bottles (e.g. from filling equipment), glass inclusion Auto-Flush Burst bottle leading to glass inclusion Manual Flush Burst bottle leading to glass inclusion | PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training Auto-Flush (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training PP – Transportation, Receiving & Storage (BAC B1.1) CCP2-P Manual Flush (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training PP – Transportation, Receiving & Storage (BAC B1.1) + Foam Inspection |
| PROCESS STEPS (Continued) |
| BT6 - Crowning | Bottle finish damage (leading to glass inclusions) | (Partially Controlled) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training + Foam Inspection/ Candling |
| BT7 – BT 8 Bottle Flush (Full Bottle Wash - external) | None identified |  |
| BT9 – Pasteurize | None identified |  |
| BT10 - Foam Inspection &/or Candling | HUMAN Physical – Failure to detect foreign matter (including glass) | PP – Personnel (BAC D1.2) Training |
| T11 – Drying (Bottle Drying and Air Knives) | None identified |  |
| BT12 – BT13 Labelling, Coding | Product not coded or not correctly coded | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) |
| BT14 – Filled Bottle Inspection | None identified |  |
| BT15 – BT18 Packing & Sealing (Divert to packers, Carton, Case Pack, Sealing) | None identified |  |
| BT19 – BT20 Secondary Code & Inspection (Secondary Packaging, Code/Inspection) | Product not coded, or not correctly coded | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) |
| BT21 – Palletize | None identified |  |
| BT22 - Storage (or Live Load) | None identified |  |
| BT23 - Shipping | None identified |  |
| PROCESS STEPS (Continued) |
| PS8 (K) - KEGGING |  |  |
| K1 - Receiving (See PS1) | None identified |  |
| K2 – K3 Storage & Handling , De-palletizing (See PS2) | None identified |  |
| K4 - External Inspection | None identified |  |
| K5 – K6 External Cleaning (Ext Wash/Inspection) | Old codes not effectively removed | PP - Recall (BAC F1.2) |
| K7 – Racking | None identified |  |
| K8 – K12 Internal Cleaning (Purge, Flush, Wash, Purge, Rinse) | None identified |  |
| K13 - Sterilize & Hold | None identified |  |
| K14 – K 15 Purge to Empty & Counter pressure | None identified |  |
| K 16 - K17 Barnes Neck Sanitize & Inspect | None identified |  |
| K18 - Filling | None identified |  |
| K19 – K 21 Barnes Neck, Wash & Sanitize | None identified |  |
| K22 - Dust Cap | None identified |  |
| K23 - Air Dry | None identified |  |
| K24 - Product Code Applied | Incorrect or missing code | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| K25 – K 26 Weigh (In-line weighing) & Palletize | None identified |  |
| K27 - Storage | None identified |  |
| PROCESS STEPS (Continued) |
| K28 - Shipping | None identified |  |
| PS8 (C) - CANNING |  |  |
| C1 - Receiving | None identified |  |
| C2 - Storage & Handling | None identified |  |
| C3 – C 4 De-palletize / Pallet ID (Collect & Timestamp Can Pallet ID, De-palletize) | Incorrect or missing code on pallet | PP - Recall (BAC F1.2) PP – Personnel (BAC D1.2) Training |
| C5 - Online visual inspection | None identified |  |
| C6 - Primary code applied | Incorrect or missing code – | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| C7 - Bulk in-line rinser | None identified |  |
| C8 – C 10 Filling (pre-evacuation & beer fill) | None identified |  |
| C11 – C13 Seaming | None identified |  |
| C14 - External Can Flush | None identified |  |
| C15 – Pasteurizer | None identified |  |
| C16 – C17 Drying | None identified |  |
| C18 - Fill Height Inspection | None identified |  |
| C19 - Divert to Packers | None identified |  |
| C20 - Hi-Cone Machine | None identified |  |
| C21 - Case Packers | None identified |  |
| C22 – Inspection (Human, visual) Inspection | None identified |  |
| PROCESS STEPS (Continued) |
| C23 – C24 Tray Machine & Code | Incorrect or missing code | PP - Recall (BAC F1.2) PP – Equipment (BAC C1.2) PP – Personnel (BAC D1.2) Training |
| C25 – Palletize | None identified |  |
| C26 - Storage (or Live Load) | None identified |  |
| C27 – Shipping | None identified |  |
| PS8 T - TANKERING |  |  |
| T1 - Empty Tanker (Receiving) | None identified |  |
| T2 - Tanker Washing/ Rinsing | None identified |  |
| T3 - Tanker Purging | None identified |  |
| T4 - Tanker Filling/ Loading | None identified |  |
| T5 – Tanker Shipping | None identified |  |
| T6 – T7 Full Tanker Receiving & Unloading | None identified |  |

| Date: | Approved by: |
| --- | --- |

# Form 9:

# Hazards not controlled by Brewery

| BAC Generic | Title: Form 9 – Hazards not Controlled by Brewery |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

| Hazards not controlled by Brewery |
| --- |
| Hazards (B = Biological, C=Chemical, P= Physical) | Indicate the way the Hazard could be Addressed (Cooking Instructions, Public Education, Use Before Date, etc.) |
| Hazard Descriptions |

# Form 10:

# HACCP PLAN

| PRODUCT NAME: BEER |
| --- |
| Process Steps | CCP/ Hazard Number | Hazard Description | Critical Limits | Monitoring procedures | Deviation Procedures | Verification Procedures | HACCP Records |
| Empty Bottle Inspection- EBI (Step BT1) | CCP1-P | Physical - Failure of the system to detect foreign matter, glass defects, bottle damage | EBI test bottle failure (i.e. 100% test bottle rejection) | Who – Packaging Operator/ QA personnel Frequency – At start up, hourly and at end of shift Refer to SOP describing EBI testing. The Packaging Operator or QA personnel signs and dates the EBI Test Bottle Monitoring Form. | If the CCP test fails, the line is stopped by Packaging Operator/ QA. Manager/ Supervisor is notified. Hold product from last successful test 100% inspection of product since last successful test is done (accept/ reject product). Repair/ fix equipment and verify. | Pre-start check completed on system by electricians. Line Supervisor reviews records after each shift or daily and signs & dates records. Monthly QA record review. | EBI Test Bottle Monitoring Records Corrective Action Records Verification Records Product Hold & Inspection Records Product Destruction Records |

| Process Steps | CCP/ Hazard Number | Hazard Description | Critical Limits | Monitoring procedures | Deviation Procedures | Verification Procedures | HACCP Records |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Empty Bottle Inspection /Residual Liquid Detector EBI/RLD (Step BT1) | CCP1-C | Chemical - Failure of the system to detect residual liquid and caustic | RLD test bottle failure (i.e. 100% test bottle rejection) | Who – Packaging Operator/ QA personnel Frequency – At start-up, hourly and at end of shift Refer to SOP describing RLD testing. The Packaging Operator or QA personnel signs and dates the RLD Test Bottle Monitoring Form. | If the CCP test fails, the line is stopped by Packaging Operator/ QA. Manager/ Supervisor is notified. Hold product from last successful test Product is discarded. | Pre-start check completed on system by electricians. Line Supervisor reviews records after each shift or daily and signs & dates records. Monthly QA record review. | RLD Test Bottle Monitoring Records Corrective Action Records Verification Records Product Destruction Records |

| Process Steps | CCP/ Hazard Number | Hazard Description | Critical Limits | Monitoring procedures | Deviation Procedures | Verification Procedures | HACCP Records |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Filling (Auto-Flush Only) (Steps BT 3- BT5) | CCP2-P | Physical – Burst bottle leading to glass inclusion | 100% functioning auto-flush (That is, the flushing spray is on, short fill cycle, reject pattern to specification). | Who – Packaging Operator Frequency– Hourly test and at end of production ; bottle burst Refer to SOP Auto-flush Monitoring Procedure Document on Auto-Flush Monitoring Form. Sign and date. | If: - System failed hourly test or - Bottle burst and system did not catch it The Operator will: - Shut off line - Run suspect bottles to reject - Flush filler - Hold product from last successful check - Re-inspect 100% of product since last successful check (accept / reject product). | Line Supervisor reviews records after each shift or daily and signs & dates records. Monthly QA record review. Annual validation of auto-flush. | Auto-Flush Monitoring Records Corrective Action Records Verification Records Annual Auto-flush Validation Records Product Hold & Inspection Records |

| Process Steps | CCP/ Hazard Number | Hazard Description | Critical Limits | Monitoring procedures | Deviation Procedures | Verification Procedures | HACCP Records |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Internal Cleaning (Manual) (Steps K8 – K12) | CCP3-C | Chemical – Cleaning solution not effectively removed. | Rinse water visible in sight glass of test keg. No detectable caustic carry-over based on phenolphthalein check. | Who - Kegging Operator Frequency – Start up, *every 24 kegs and at the completion of kegging operation Perform a visual check for rinse water and phenolphthalein check for caustic carry over Refer to SOP for details. Note: Frequency of ‘every 24 Kegs’ is for example purposes only. Frequency should be determined based off current operations (i.e. rate and number of bottles produce) | If the CCP fails: The Kegging Operator notifies the Line Supervisor and describes the failure. If the rinse water is not visible through the sight glass and/or the phenolphthalein check is positive for caustic (turns pink), the Kegging Operator performs 2 additional test keg runs and if either of the re-test fails a CCP failure has occurred. If both re-test passes, production may resume. Production may resume when the problem has been corrected and confirmed by 2 consecutive test keg runs. | QA personnel will perform a sodium check on the test keg from the start of each production run. Sodium in the test keg sample must meet the Canadian Drinking Water Guidelines of <200mg/L of sodium. The Supervisor verifies the keg rinse reports daily. | Keg Cleaning Records Analytical Results Corrective Action Report Verification Reports CCP Monthly Audit CCP Training Records |

| Process Steps | CCP/ Hazard Number | Hazard Description | Critical Limits | Monitoring procedures | Deviation Procedures | Verification Procedures | HACCP Records |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Internal Cleaning (Manual) (Steps K8 – K12) | CCP3-C |  |  |  | If the CCP failure occurs during production, production is stopped and all kegs are put on hold back to the last good check. All held product is 100% discarded. Deviations and Corrective Actions are recorded on the Corrective Action Report by the Supervisor. | QA performs a CCP audit on a monthly basis. |  |

| Date: | Approved by: |
| --- | --- |

# HACCP PLAN
appendices

## appendix 1

## form 3

## information used for flowcharts

Major Process Steps (Ps) for Making Beer

| INPUT | PROCESS STEP/ ID | OUTPUT |
| --- | --- | --- |
| Dry Ingredients | PS1 | Receiving |  |
|  | PS2 | Storage & Handling |  |
| Barley Malt, Wheat Malt, Cereal Grains, Water, Water Preparation Agents, Hops, Other ingredients | PS3 | Brewing - - Milling - Mashing - Lautering - Kettle - Whirlpool - Cooling | Spent grains (by-product), Hot Water, Trub, Wort, Cold Water |
| Other Ingredients( processing aids), Yeast | PS4 | Fermentation | Yeast, Pitching Yeast |
| Other Ingredients( processing aids) CO2 | PS5 | Aging - Clarification - Filtration | Beer, CO2 (collection, waste) Bulk Beer |
|  | PS6 | Bright Beer Storage |  |
|  | PS7 | Bright Beer Processing | Bright Beer |
| Packaging Materials, New Bottles (NB), Returned Bottles (RB), Kegs, Tankers, Cans | PS8 | Packaging |  |
|  | PS9 | Warehousing/Shipping |  |

Ps3 - Brewing

| INPUT | PROCESS STEP/ ID | OUTPUT |
| --- | --- | --- |
| Liquid/ Dry/ Bulk Compressed Air | B1 | Receiving (See PS1) |  |
|  | B2 | Storage (See PS2) |  |
| Barley Malt, Wheat Malt | B3 | Milling | Malt Dust, Grist |
| Cereal, Prepared Brewing Water, Steam | B4 | Cereal Cooker | Cooked Cereal |
| Prepared Brewing Water,Steam, Grist | B5 | Mashing (Mash Mixer, Mash Cooker) | Mash |
| Sparge water, Steam | B6 | Lautering (Lauter Tun, Mash Filter removal of spent grains | Spent Grains, Sweet Water |
|  | B7 | Holding Tank |  |
| Hops, Hop oil, other ingredients (eg. syrup), Steam | B8 | Kettle |  |
|  | B9 | Whirlpool/ Centrifuge/ Hot Wort Tank |  |
| Oxygen | B10 | Wort Cooling (Heat Exchanger) | Cooled Wort |
| Next process - PS4 Fermentation |

Ps4 - Fermentation

| INPUT | PROCESS STEP/ ID | OUTPUTS |
| --- | --- | --- |
| Oxygen or sterile air, Cold Wort | F1 | Wort Oxygenation/ Wort Aeration | Aerated/ Oxygenated Wort |
| Cooled aerated wort, Dry Hop, Pitching yeast (See PS3 – Brewing) | F2 | Fermentation | CO2 |
| (Cooling Step) | F3 | Cooling | Yeast |
|  | F4 | Green Beer | Green Beer, |
| Next Process – PS5 Aging (Primary Storage) |

Sub-Process - Yeast Preparation

| INPUT | PROCESS STEP/ ID | OUTPUTS |
| --- | --- | --- |
| Yeast Source, New Culture Oxygenated Wort, Aerated Wort, Nutrients | Y1 | Propagation | Pitching Yeast |
| Pitching Yeast (Cooling Step) | Y2 | Storage | Waste Yeast |
| Acids, Phosphoric, Sulphuric | Y3 | Acid Washing | Pitching Yeast Waste Yeast |
| Next Process – F2 Fermentation |

Ps5 - Aging/Clarification/Filtration

| INPUT | PROCESS STEP/ ID | OUTPUTS |
| --- | --- | --- |
| Green Beer (See PS4 - Fermentation) | A1 | Cooling |  |
|  | A2 | Buffer Tank |  |
|  | A3 | Centrifuge | Yeast/ Spent Waste (by-product) |
| Processing Aids, Stabilizers, CO2 Preservatives | A4 | Buffer tank | CO2 |
|  | A5 | Cooling |  |
| CO2, Hops | A6 | Aging Tank | Beer, Spent Hops, CO2 |
| De-aerated Water, Processing Aids, Stabilizers, CO2 Preservatives | A7 | Secondary Storage | Spent Yeast, CO2 |
| De-aeration Water, Processing Aids, Stabilizers, CO2 Preservatives | A8 | Surge/ buffer Tank | CO2 |
| Caramel and other ingredients, Processing Aids, Stabilizers, CO2, Nitrogen Preservatives | A9 | DE Pre-filter/ Filter Trap/ Sheet Filter/ Membrane Filter/ PVPP Filter | Spent DE, Spent Yeast, Spent Hops, CO2, |
| CO2, De-aerated Water, Nitrogen | A10 | Bright Beer Storage | Bright Beer, O2 |
| Next Process – PS7 Bright Beer Processing |

Ps7 - Bright Beer Processing

A – Sterile Filtration

| INPUT | PROCESS STEP/ ID | OUTPUTS |
| --- | --- | --- |
| Filter Preparation (Membrane Filters, Candle Filters, Integrity Test, Re-chill) CIP Chemicals, Steam, Water, Coolant, Sterile Gases | SF1 | Bright Beer Tank | Effluent |
| Bright Beer, CO2 | SF2 | Sterile Filtration | Sterile Beer |
|  | SF3 | Sterile Beer Tank |  |
| Next Process – PS8 Packaging |

B – Flash Pasteurization

| INPUT | PROCESS STEP/ ID | OUTPUTS |
| --- | --- | --- |
| Bright Beer Steam , hot water, coolant, CO2 | FP1 | Flash pasteurization | Pasteurized Beer Effluent |
|  | FP2 | Pasteurized Beer Tank |  |
| Next Process – PS8 Packaging |

Packaging Processes - Ps8 (RB)

Returned Bottles Prep (Float Glassware Prep)

| INPUT | PROCESS STEP/ ID | OUTPUT |
| --- | --- | --- |
| Returned (Float) Glassware | RB1 | Receiving/ Storage |  |
|  | RB2 | De-palletizing | Pallets, Straps, Film, Twine |
|  | RB3 | De-casing | Foreign materials, Scrap cartons, Scrap Partitions, Damaged Broken Glass, crowns |
|  | RB4 | Human (Visual) Inspection | Foreign materials, Scrap cartons, Scrap Partitions, Damaged Broken Glass, crowns |
|  | RB5 | Bottle Wash Loading | Waste beer, debris |
| First Post Soak | RB6 | Pre-rinse sprays | Straws, butts, waste water |
| Steam, water, chemicals | RB7 | Soak Tanks With Caustic | Label pulp, Caustic (Sodium Hydroxide), Plastic |
| Caustic Solution | RB8 | Hydro Jet Sprays |  |
| Receive Ext Flush | RB9 | Post-Soak | Recovered post soak (effluent) |
| Recovered External/ Internal | RB10 | External Flush | Recovered external flush |
| Recovered Final Rinse | RB11 | External and internal Rinse | Recovered external rinse, label pulp carryover |
| Potable Water | RB12 | Interior Final Rinse | Recovered final rinse |
| Potable Water | RB13 | External Final Rinse | Recovered final rinse Washed Glassware |
| Next Process – PS8 BT - Bottling |

Packaging Processes - Ps8 (NB)

New Bottles (Glassware) Prep

| INPUT | PROCESS STEP/ ID | OUTPUT |
| --- | --- | --- |
| New Glassware | NB1 | Receiving |  |
|  | NB2 | Preliminary Inspection | Reject loads and pallets |
|  | NB3 | Storage |  |
|  | NB4 | Collect the Manufacturing Pallet tags |  |
|  | NB5 | Pallet prep | Straps, film |
|  | NB6 | De-palletize | Top frame, tier sheet, pallets |
|  | NB7 | Visual Inspection | Rejects, damaged glassware |
|  | NB8 | Bottle Loading |  |
| Potable Water, Compressed Air | NB9 | Bulk Glass Rinser | Rinsed glassware Rinse Water effluent |
| Next Process – PS8 BT - Bottling |

Packaging Processes - Ps8 (BT)

Bottling

| INPUT | PROCESS STEP/ ID | OUTPUT |
| --- | --- | --- |
| Washed and Finished Glass, (New or Float) Compressed Air, Conveyor Lubricant, Conveyor Flush Water, | BT1 | Empty Bottle Inspection | Rejects, Finished Water and Lube |
|  | BT2 | Down bottle filler in-feed control | Rejects |
| CO2, Compressed Air, Potable Water, Lube Water | BT3 | Purges & Evacuation & Positive Pressure | Glass, debris, shards CO2 |
| CO2, Counter pressure bowl, Bright Beer, Hot Pressurized Water, Filter Pressurized Water | BT4 | Filling | Bottle breakage, CO2 |
|  | BT5 | Fobbing | Beer foam overflow |
| Packaging Materials, Crowns, Compressed air, City Water flush, Lubricants | BT6 | Crowning | Damaged crowns, water effluent, bottle breakage, spilled beer |
| City Water Flush | BT7 | Crowner Flush (external) | Water and beer effluent |
| City Water | BT8 | Filled Bottle wash external | Rejects |
| Water, Steam, Chemicals | BT9 | Pasteurize | Effluent, broken glass |
|  | BT10 | Foam Inspection/ Candling Inspection | Rejects |

Packaging Processes - Ps8 (BT) (Continued)

Bottling (Continued)

| INPUT | PROCESS STEP/ ID | OUTPUT |
| --- | --- | --- |
| Ambient air blower | BT11 | Bottle Drying and Air Knives |  |
| Packaging material, adhesive, compressed air | BT12 | Labelling | Bottle breakage, labels, adhesive, beer |
| Packaging material (ink) | BT13 | Primary Packaging, Coding | Inks, Cleaning Solutions |
|  | BT14 | Filled Bottle Inspection | Rejects |
|  | BT15 | Divert to packers |  |
| Packaging material, cartons, adhesive, partitions (inserts) | BT16 | Carton Forming | Rejects, damaged |
|  | BT17 | Case Packing | Bottle breakage, beer, damage |
| Packaging Material - Adhesive | BT18 | Case Sealing | Bottle breakage, beer, damage |
| Packaging Material – Ink | BT19 | Secondary Packaging Code | Inks, Cleaning Solutions |
|  | BT20 | Full Case Inspection | Rejects |
| Pallets, Tier sheets, trays, straps, shrink wrap, pallet ID | BT21 | Palletize | Finished Goods |
| Finished Goods | BT22 | Storage (or Live Load) |  |
|  | BT23 | Shipping |  |

Packaging Processes - Ps8 (K)

Kegging

| INPUT | PROCESS STEP/ ID | OUTPUT |
| --- | --- | --- |
| Keg Float, Keg Caps, Bright Beer | K1 | Receiving (See PS1) |  |
|  | K2 | Storage & Handling (See PS2) |  |
|  | K3 | De-palletizing (See PS2) |  |
|  | K4 | External Inspection | Rejected Kegs |
| Water & Detergents | K5 | Ext Wash | Dust caps, labels, effluent |
|  | K6 | Post Wash Inspection | Temporary storage |
| Kegs Temperature Storage | K7 | Racking |  |
| Compressed Air | K8 | Purge to Empty | Waste beer, rejected kegs |
| Potable Water | K9 | Flush | Rinsings |
| Acid Steam & Sodium Hydroxide | K10 | Wash | Drain or recover |
| Compressed Air | K11 | Purge to empty | Residual CIP solution |
| Heated Water | K12 | Rinse | Rinsings to drain |
| Steam | K13 | Sterilize & Hold |  |
| CO2 | K14 | Purge to Empty | Residual Water, CO2 |
| CO2 | K15 | Counter Pressure | CO2 |
| Steam | K16 | Barnes Neck Sanitize | Fill |
|  | K17 | Inspect | Rejected Keg |

Packaging Processes - Ps8 (K) (Continued)

Kegging (Continued)

| INPUT | PROCESS STEP/ ID | OUTPUT |
| --- | --- | --- |
| Bright Beer, Clean Kegs from storage | K18 | Filling | Waste Beer |
| Steam | K19 | Sterilize Barnes Neck | Condensate |
| Chlorinated Water | K20 | Final Rinse Dome | Chlorinated water to drain |
| Sanitation chemicals | K21 | Chemical Sanitize Barnes Neck |  |
| Packaging Material | K22 | Dust Cap |  |
| Plant air | K23 | Air Dry |  |
| Packaging Material | K24 | Product Code Applied |  |
|  | K25 | In-line weighing |  |
|  | K26 | Palletize | Full goods storage |
|  | K27 | Storage or Live Load |  |
|  | K28 | Shipping |  |

Packaging Processes - Ps8 (C)

Canning

| INPUT | PROCESS STEP/ ID | OUTPUT |
| --- | --- | --- |
| Cans, Can ends, Bright Beer (from Ps7) | C1 | Receiving | Damaged Cans |
|  | C2 | Storage & Handling |  |
|  | C3 | Collect & Timestamp Can Pallet ID | Straps (to scrap/ recycle) |
|  | C4 | De-palletize to mass conveyor | Pallet, frame (top), tier sheet |
|  | C5 | Online visual inspection | Non-conforming cans (rejects) |
| Packaging Material (ink) | C6 | Primary code applied | Ink |
| Treated water filtered | C7 | Bulk in-line rinser | Rinse water (Bulk Rinse discharge water) |
| CO2 & Bright beer | C8 | Filling (pre-evacuation & beer fill) | Open filled cans |
| Open filled cans & CO2 | C9 | Bubble breakers | CO2 |
| CO2 | C10 | Under Cover Gassing | CO2 |
| Can ends | C11 | Collect manufacturing lot detail for ends | Paper sleeves to baler |
| Continuous lubrication | C12 | Double seaming | Excess/ surplus lube, Beer |
|  | C13 | Filler valve monitor | Reject cans |
| Rinse water (Bulk Rinse discharge water) | C14 | External Can Flush | Water to sewer |

Packaging Processes - Ps8 (C) (Continued)

Canning (Continued)

| INPUT | PROCESS STEP/ ID | OUTPUT |
| --- | --- | --- |
| Heating, City Water, Water Treatment | C15 | Pasteurizer | Second cooling water to drain |
| Ambient Air | C16 | Pre-Blower Station |  |
| Compressed Air, Ambient Air | C17 | Final Dryer Station |  |
|  | C18 | Fill Height Inspection | Reject cans |
|  | C19 | Divert to Packers | Finished Cans |
| Open Format 6’s & 8’s, Hi-Cone Web, Finished Cans | C20 | Hi-Cone Machine |  |
| Closed format 12’s & 24’s, cartons, Finished Cans | C21 | Case Packers |  |
|  | C22 | Visual Inspection | Rejects, cans, Hi-cone, cartons |
| Trays, Hot Melt | C23 | Tray Machine | Reject Trays |
| Packaging Material (ink) | C24 | Secondary Code applied | Ink |
| Pallets & Stretch film | C25 | Transfer to Palletizer | Finished Pallets |
| Finished Pallets | C26 | Storage (or Live Load) |  |
|  | C27 | Shipping |  |

Ps8 (T)

Tankering

| INPUT | PROCESS STEPS/ ID | OUTPUT |
| --- | --- | --- |
|  | T1 | Empty Tanker |  |
| Caustic Water, Acid | T2 | Tanker Washing |  |
| City Water, CO2 | T3 | Tanker Purging | Clean Tanker, CO2 |
| Bright Beer, Clean Tanker | T4 | Tanker Filling |  |
|  | T5 | Tanker Shipping |  |
|  | T6 | Full Tanker Receiving |  |
|  | T7 | Full Tanker Unloading |  |

Other Sub-Process - Co2

(No Flowchart)

| INPUT | PROCESS STEP/ ID | OUTPUTS |
| --- | --- | --- |
| Collected CO2 | CO1 | Increase Pressure (Booster) |  |
|  | CO2 | Scrubbers (remove water soluble compounds) | Water soluble compounds |
|  | CO3 | Carbon Filters - Deodorizer |  |
|  | CO4 | Carbon Filters – Dust Filters | Particulate Material |
|  | CO5 | Compressor |  |
|  | CO6 | Dryers | Moisture |
|  | CO7 | Particulate Filter | Particulate Material |
|  | CO8 | CO2 Condensers |  |
| CO2 Purchase | CO9 | Liquid Storage |  |
|  | CO10 | Vaporization |  |
|  | CO11 | High Pressure Carbon Filters |  |
|  | CO12 | Particulate Filters | CO2, Particulate Material |

Other Sub-Process - Water Processing

(No Flowchart)

| INPUT | PROCESS STEPS | OUTPUTS |
| --- | --- | --- |
| Water Source – City, Well, Purchased | W2 Purification: Reverse Osmosis, UV, Ozonation, Chlorination, Filtration (Sand, DE, Activated carbon, multimedia) | Purified Water (2) |
| Purified Water (2) | W3 Storage |  |
| Acids, Salts, Steam Purified Water | W4 Brewing Water Preparation, pH adjustments, Salts addition | Mash Water Sparge Water |
| CO2 | W5 De-aeration, Cooling, Carbonation | Line Packing or Push Water Dilution Water for High Gravity CO2 |

## appendix 2

## form 8
CRITICAL COTNROL
POINTS
(low alcohol beer)

| BAC Generic | Title: Form 8 – Critical Control Points (Low Alcohol Beer) |
| --- | --- |
|  | Completed By: BAC TC | Date: |
|  | Approved By: BAC TC | Date: |

| Incoming material/ process step/ hazards on schematic diagram | Category and identified hazard. | Determine if fully controlled by Pre-requisite program. *If “yes” = indicate “Pre-requisite Program” and proceed to next identified hazard. *If “no” = proceed to question1 (Q1). | Q1. Could a control measure(s) be used by the operator at any process step? If NO = not a CCP + identification on how this hazard will be controlled before and after the process + proceed to the next identified hazard If YES = description + next question (Q2) | Q2. Is it likely that contamination with the identified hazard could occur in excess of the acceptable level or could increase to an unacceptable level? If NO = not a CCP + proceed to the next identified hazard If YES = next question (Q3) | Q3. Is this process step specifically designed to eliminate/reduce the likely occurrence of the identified hazard to an acceptable level? If NO = next question (Q4) If YES = CCP + go to last column | Q4. Will a subsequent step eliminate the identified hazard or reduce likely occurrence to an acceptable level? If NO = CCP + go to last column If YES = not a CCP + identify subsequent step + proceed to the next identified hazard | CCP Number + proceed to next identified hazard |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Process Step (For Low Alcohol Beer Only) |  |  |  |  |  |
| PS3 - AGING/ CLARIFICATION/ FILTRATION |  |  |  |  |  |  |
| A10 – Bright Beer Storage | Biological – Inadequate pH adjustment to control Clostridia growth downstream Chemical – None identified Physical – None identified | No | Yes | Yes | Yes |  | CCP4-B |

| Date: | Approved by: |
| --- | --- |

## appendix 3

## form 10

## additions for
low alcohol beer

LOW ALCOHOL BEER ONLY

| PRODUCT NAME: |
| --- |
| Process Steps | CCP/Hazard Number | Hazard Description | Critical Limits | Monitoring procedures | Deviation Procedures | Verification Procedures | HACCP Records |
| Bright Beer Storage (Step A10) | CCP4-B (Note: This is an arbitrary number. CCP numbering will depend on the number of CCPs found in individual breweries CCPs) | Inadequate pH adjustment to control Clostridia growth downstream | pH <4.5 | pH analysis of wort in kettle by QA | pH must be less than 4.4 at kettle wort sample in kettle - If pH greater than or equal to 4.4 will add additional acid to kettle & recheck. - If pH greater than or equal to 4.4 QA manager (or designate) notified and a deviation report must be completed | pH analysis performed on each kettle wort cooler sample & result reviewed by QA manager or designate (if greater than pH 4.5 will reprocess and recheck) pH analysis performed on each BBT & result reviewed by QA manager or designate (if greater than pH 4.5 will reprocess and recheck) pH analysis performed on each filler start up sample & result reviewed by QA manager or designate (if greater than pH 4.5 will dump product) Calibration of pH meter & control checks of 5 samples prior to run. After each production the QA Manager or designate verifies the calibration records for BBT approvals. QA Manager conducts yearly audit of lab analyses. | Lab reports Calibration records Audit records |

| Date: | Approved by: |
| --- | --- |

## appendix 4

## diagrams for 
hazard identification & ccp decision tree

Diagrams for Hazard Identification and CCP Decision Tree

Critical Control Points for breweries were determined using the HACCP Decision Tree.  The Decision Tree was first developed by a Codex Alimentarius working group on HACCP in June 1991.

4.1 Hazard Determination

##### These questions are to be answered for each potential hazard at each step:

* Not a hazard to be controlled at this step.

4.2 CCP Decision Tree

Pre-screening question –

Determine if (hazard) fully controlled by Pre-requisite programs.  If ‘yes’, indicate “Pre-requisite Program(s)” and proceed to the next identified hazard.  If ‘no’, proceed to Question 1 below.

###### Q1

###### Q2

###### Q3

###### Q4

## appendix 5

## bac glass inclusion reference

BAC Glass Inclusion Reference

The Critical Control Points for the brewing industry have been identified through analysis as described in preceding sections.

In 1988, a BAC Glass Integrity Task Force developed a manual entitled Good Manufacturing Practice on the Prevention of Glass Inclusion in Finished Product.  As its name implies, it was intended to ensure that product entering the market contained no glass contaminants. The GMP was updated 1998 to deal with changes in the industry and technology in the last 10 years.

The GMP deals specifically with:

Environmental Controls

- Preventive Measures

- Regular Maintenance Checks

Prewash Bottle Handling

- Preventive Measures

- Corrective Measures

Bottle Washing

- Preventive Measures

Bottle Conveying Systems

- Preventive Measures

- Corrective Actions

Washed Bottle Inspection

- Inspection Methods

- Maintenance Measures

- Corrective Measures

BAC Glass Inclusion Reference (Continued)

Filling and Crowning Operations

- Corrective Measures for Glass Inclusions

- Continual Incident Levels

Filled Bottle Inspections

- Uncrowned, Improperly Crowned and Low-Filled Bottles

- Foam-Picking

- Candling

- Filtration

- Reaction to Inclusions

Verification and Monitoring for GMP

- Written Procedures

- Setup and Maintenance Checklists

- Production Records

- Quality Checklists

- Consumer Incidents Correlation

This document will be helpful in developing individual brewery HACCP Programs.  Copies of the manual may be obtained by contacting:

Brewers Association of Canada
100 Queen Street, Suite 650
Ottawa, Ontario  K1P 1J9
Telephone:  (613) 232-9601  Fax:  (613) 232-2283
E-mail:  office@brewers.ca

## appendix 6

## blank forms 1 - 10

| PRODUCT DESCRIPTION FORM 1 |
| --- |
| PROCESS/PRODUCT TYPE NAME: |
| 1. Product Name(s) |  |
| 2. Important Product Characteristics (Aw, Ph, Preservatives,...) |  |
| 3. How it is to be Used |  |
| 4. Packaging |  |
| 5. Shelf Life |  |
| 6. Where it will be Sold |  |
| 7. Labelling Instructions |  |
| 8. Special Distribution Control |  |

| Date: | Approved by: |
| --- | --- |

LIST OF PRODUCT INGREDIENTS AND INCOMING MATERIALS FORM 2

PRODUCT NAME:

| Date: | Approved by: |
| --- | --- |

PROCESS FLOW DIAGRAM FORM 3

PRODUCT NAME(S):

| Date: | Approved by: |
| --- | --- |

PLANT SCHEMATIC FORM 4

PRODUCT NAME(S):

| Date: | Approved by: |
| --- | --- |

| HAZARDS IDENTIFICATION FORM 5 |
| --- |
| PRODUCT NAME(S) List all biological hazards related to ingredients, incoming material, processing, product flow, etc. |
| IDENTIFIED BIOLOGICAL HAZARDS (Bacteria, Parasites, Viruses...) | CONTROLLED AT |

| Date: | Approved by: |
| --- | --- |

| HAZARDS IDENTIFICATION FORM 6 |
| --- |
| PRODUCT NAME(S) List all chemical hazards related to ingredients, incoming material, processing, product flow, etc. |
| IDENTIFIED CHEMICAL HAZARDS | CONTROLLED AT |

| Date: | Approved by: |
| --- | --- |

| HAZARDS IDENTIFICATION FORM 7 |
| --- |
| PRODUCT NAME(S) List all physical hazards related to ingredients, incoming material, processing, product flow, etc. |
| IDENTIFIED PHYSICAL HAZARDS | CONTROLLED AT |

| Date: | Approved by: |
| --- | --- |

| CCP DETERMINATION FORM 8 |
| --- |
| Process Step/ Incoming Material | Category and identified Hazard Fully controlled by Pre-requisite program? *If yes indicate and proceed to next identified hazard *If no proceed to (Q1) | Q1. Could a control measure(s) be used at any process step? *If no = not CCP. Identify how this hazard will be controlled before and after the process and proceed to next identified hazard. *If yes = describe and proceed to (Q2) | Q2. Is it likely that contamination with the identified hazard could occur in excess of the acceptable level or could increase to an unacceptable level? *If no = not CCP. Proceed to next identified hazard *If yes = proceed to (Q3) | Q3. Is this process step specifically designed to eliminate/reduce the likely occurrence of the identified hazard to an acceptable level? *If no = proceed to (Q4) *If yes = CCP. Go to last column | Q4. Will a subsequent step eliminate the hazard or reduce its likely occurrence to an acceptable level? *If no = CCP. Go to last column *If yes = not a CCP. Identify subsequent step and proceed to the next identified hazard | CCP Number *Proceed to the next identified hazard |

| Date: | Approved by: |
| --- | --- |

| HAZARDS NOT CONTROLLED BY OPERATOR FORM 9 |
| --- |
| PRODUCT NAME(S) List here any biological, chemical and physical hazards which are not controlled by the Operator. |
| HAZARDS | INDICATE THE WAY THE HAZARD COULD BE ADDRESSED (COOKING INSTRUCTIONS PUBLIC EDUCATION, USE BEFORE DATE,..). |

| Date: | Approved by: |
| --- | --- |

| HACCP PLAN FORM 10 PRODUCT NAME: |
| --- |
| Process Steps | CCP/Hazard Number | Hazard Description | Critical Limits | Monitoring Procedures | Deviation Procedures | Verification Procedures | HACCP Records |

| Date: | Approved by: |
| --- | --- |

## appendix 7

## reference literature

References

Procedures to Implement the Hazard Analysis Critical Control Point System.  International Association of Milk, Food and Environmental Sanitarians, Inc. Ames, Iowa. 1991

Micro-organisms in foods, Book 4.  Application of the hazard analysis critical control point (HACCP) system to ensure microbiological safety and quality.  The International Commission on Microbiological Specifications for Foods (ICMSF). Blackwell Scientific Publications. Oxford. 1988.

Food Safety Enhancement Program. Volumes 1 - 4. Agriculture Canada. 1993-7.

A Simple Guide to Understanding and Applying The Hazard Analysis Critical Control Point Concept. 2nd edition.  international Life Sciences Institute.  1997

CFIA Generic HACCP Plan Models
http://www.inspection.gc.ca/english/fssa/polstrat/haccp/manue/ch2sec3-45e.shtml#2.4

# Footnotes

Output from one step may be used as input to another step (indicated by bolded print)

# Text boxes

Will a subsequent step eliminate the identified hazard or reduce its likely occurance to an acceptable level?

No

Yes = CCP

Is this process step specifically designed to eliminate or reduce the likely occurance of this identified hazard to an acceptable level?

Not a CCP.  Proceed to next identified hazard.

Yes

No

Is it likely that contamination with the identified hazard could occur in excess of the acceptable level or could increase to an unacceptable level?

Not a CCP.  Identify how this hazard will be controlled before or after the process and proceed to next identified hazard.

C.M.(S) exists

No C.M. exists

Could a control measure(s) be used by the operator at any process step?

NO

YES

Is reduction, if any at a further step adequate?

HAZARD

No Hazard*

YES

NO

NO

YES

Is an unacceptable level, survival, persistence or increase at this step probable?

Is an unacceptable contamination at this step probable?

No Hazard*

YES

YES

NO

Not a CCP.  Proceed to next identified hazard.

Yes

No = CCP

NO

Is the presence of a potential hazard in raw material probable?

Is the presence of a potential hazard in the line or the environment probable?