HACCP Plan Workbook

A comprehensive workbook for Canadian Breweries to develop and implement a company

specific HACCP Plan

A Project of
Brewers Association of Canada
HACCP Working Group

Revision Date:  November 2011
www.brewers.ca

HACCP Workbook

# Copyright and Contact Information

### BAC Food Safety Standard

Copyright © 2011 Brewers Association of Canada

All rights reserved.  No part of this material may be reproduced, stored in a retrieval system or transmitted in any form or by any means (e.g. electronic, mechanical, photocopying, recording, or otherwise), without the prior written permission of Brewers Association of Canada.

While the developers of this document have made every effort to ensure that the information contained herein is accurate and complete at the time of issuance, the Brewers Association of Canada, its members, and the members of the development committees cannot be held liable for errors or omissions.  Application of these documents is at the user’s discretion only.  It is suggested that potential users confirm, in advance, the applicability of these documents to their specific needs.

Users of these documents are encouraged to make suggestions regarding content, format, or other suggestions concerning potential modifications or upgrades for future editions.

Please address your comments to:

Mr./ Mrs.

Director,

Brewers Association of Canada

Ottawa, Ontario

Canada

Telephone: (613) 232-9601

Facsimile:   (613) 232-2283

HACCP Workbook Index

Date Program Approved by Establishment (d/m/y):	____________________

Approval Signature:  ______________________________________________

| Contents | Pages |
| --- | --- |
| Copyright and Contact Information | 3 |
| Introduction | 7 |
| Instructions: |  |
| Form 1: Product Description | 15 |
| Form 2: List of Product Ingredients and Incoming Materials | 19 |
| Form 3: Process Flow Diagram | 26 |
| Form 4: Plant Layout with Employee/Product Flow | 38 |
| Form 5: Biological Hazard Identification | 42 |
| Form 6: Chemical Hazard Identification | 46 |
| Form 7: Physical Hazard Identification | 50 |
| Form 8: Critical Control Point Determination | 54 |
| Form 3A: Process Flow Diagram with CCPs | 58 |
| Form 5A: Biological Hazard Identification and Control | 62 |
| From 6A: Chemical Hazard Identification and Control | 66 |
| Form 7A: Physical Hazard Identification and Control | 70 |
| Form 9: Hazards Not Controlled by Operator | 74 |
| Form 10: HACCP Plan | 78 |

Table of Contents

Copyright and Contact Information	3

HACCP Workbook Index	4

INTRODUCTION	7

HACCP Plan Document Control	11

How to use the BAC HACCP Workbook :	12

HACCP Development Flow Chart	14

Form 1 – Product Description	15

How to complete Form 1	16

Blank Form 1	17

Form 2 – List of Product Ingredients and Incoming Materials	19

How to complete Form 2	20

Blank Form 2	24

Form 3 – Process Flow Diagram	27

How to complete Form 3	28

Blank Form 3	36

Form 4 – Plant Layout with Employee/Product Flow	39

How to complete Form 4	40

Example of Form 4	41

Form 5 – Biological Hazard Identification	43

How to complete Form 5	44

Blank Form 5	45

Form 6 – Chemical Hazard Identification	47

How to complete Form 6	48

Blank Form 6	48

Form 7 – Physical Hazard Identification	51

How to complete Form 7	52

Blank Form 7	52

Table of Contents (Continued)

Form 8 – Critical Control Point Identification	55

How to complete Form 8	56

Blank Form 8	56

Form 3A – Process Flow Diagram with CCPs	59

How to complete Form 3A	60

Blank Form 3A	60

Form 5A – Biological Hazard Identification and Control	63

How to complete Form 5A	64

Blank Form 5A	64

Form 6A – Chemical Hazard Identification and Control	67

How to complete Form 6A	68

Blank Form 6A	68

Form 7A – Physical Hazard Identification and Control	71

How to complete Form 7A	72

Blank Form 7A	72

Form 9 – Hazards Not Controlled by Operator	75

How to complete Form 9	76

Blank Form 9	76

Form 10 – HACCP Plan	79

How to complete Form 10	80

Components of Form 10	81

Blank Form 10	81

Introduction

HACCP Workbook

This Workbook has been designed so that the user may identify the components of the BAC Generic HACCP Plan that apply to their operation and, with the assistance of instructions and trained personnel, transfer and/or modify the applicable contents onto the blank forms and thereby develop a customized HACCP Plan.

What is HACCP?

Hazard Analysis and Critical Control Points (HACCP) is a preventative food safety management system that controls, eliminates, and/or minimizes biological, chemical, and physical, hazards from harming customers.  A complete HACCP system includes a documented, verified Prerequisite Program (Good Manufacturing Practices) and identifies potential hazards with a HACCP Plan.

The workbook contains Forms 1 through 10, as identified in the BAC Generic HACCP Plan.  Users of this workbook are advised to utilize all forms as they are presented, however experienced HACCP practitioners may elect to combine forms 5, 6 and 7 into a single form in order to reduce the size of their final document.  If a combined-form process is followed, the ingredient and hazard analysis must still be conducted on a line-by-line basis.

Canadian Food Inspection Agency (CFIA)

This HACCP Workbook is reflective of the BAC Generic HACCP Plan, which in turn has been developed according to the CFIA Food Safety Enhancement Program (FSEP) requirements.  The following are statements provided on the CFIA website (www.inspection.gc.ca):

- Hazard Analysis Critical Control Point (HACCP) has become synonymous with food safety.  It is a worldwide recognized, systematic and preventative approach that addresses biological, chemical and

Canadian Food Inspection Agency (CFIA)  (Continued)

physical hazards by anticipating and preventing, rather than by finished production inspection.

- The HACCP system for managing food safety concerns grew from two major developments.  The first breakthrough was associated with Dr. W.E. Deming, whose theories of quality management are widely regarded as a major factor in turning around the quality of Japanese products in the 1950's.  Dr. Deming and others developed Total Quality Management (TQM) systems that emphasized a total systems approach to manufacturing that could improve quality while lowering costs.

- The second major breakthrough was the development of the HACCP concept itself.  The HACCP concept was pioneered in the 1960's by the Pillsbury Company, the U.S. Army and NASA as a collaborative development of the production of safe foods for the space program.  NASA wanted a "zero defects" program to guarantee safety in the foods that astronauts would be consuming in space.  Pillsbury therefore introduced and adopted HACCP as a system that could provide the greatest safety while reducing dependence on finished product sampling and testing.  HACCP emphasized control of the process as far upstream in the processing system as possible by utilizing operator control and/or continuous monitoring techniques at critical control points.  Pillsbury presented the HACCP concept publicly at a conference for food protection in 1971.  The use of HACCP principles in the promulgation of low acid canned food regulations was completed in 1974 by the U.S. Food and Drug Administration (FDA).  In the early 80s, the HACCP approach was adopted by other major food companies.

Canadian Food Inspection Agency (CFIA)  (Continued)

- The National Academy of Science (USA) recommended in 1985 ("the Green Book") that the HACCP approach be adopted in food processing establishments to ensure food safety.  More recently, there have been recommendations for the broad application of HACCP to food safety from numerous groups (e.g. International Commission for Microbiological Standards for Foods (ICMSF), International Association of Milk, Food and Environmental Sanitarians (IAMFES)).

- The Codex Alimentarius (FAO/WHO) Food Hygiene Committee mandated a working group in 1991 that has developed guidelines for HACCP application. This document has been well received and is getting wide international acceptance.

The following sequence of 12 steps is the recommended approach for the development of a HACCP program:

  - Assemble HACCP team

  - Describe product

  - Identify intended use

  - Construct process Flow Diagram and Plant Schematic

  - Conduct on-site verification of Flow Diagram and Plant Schematic

  - Identify hazards. List preventative measures to control them
- (principle 1)

  - Determine Critical Control Points - (principle 2)

  - Establish limits at each Critical Control Point - (principle 3)

  - Establish procedures to monitor Critical Control Points - (principle 4)

  - Establish corrective action to take in case of a deviation - (principle 5)

  - Establish procedures to verify systems are working correctly
- (principle 6)

  - Establish effective record keeping - (principle 7)

Canadian Food Inspection Agency (CFIA)  (Continued)

This logic sequence has been agreed to at the international level by a HACCP working group of Codex Alimentarius (WHO/FAO). The seven basic principles of HACCP are indicated in the brackets.

What is the BAC Generic HACCP Plan?

The BAC Generic HACCP Plan is a set of forms (based on the Canadian Food Inspection Agency (CFIA) – Food Safety Enhancement Program (FSEP)) which analyzes brewery operations in two ways:

- Product Ingredients and Packaging Materials; and

- Process Flow: This includes the generic process flow that occurs from receiving and through the brewing process.

How to develop a HACCP Plan:

Step 1:	Acquire full commitment from management and all levels of the organization.

Step 2:	Choose a food safety team of three to five dedicated individuals.  This team should consist of people that hold various positions within the company (e.g. Management, sanitation employee, etc.).

Step 3:	A customized Prerequisite Program should be developed before the customized HACCP Plan.  The BAC Prerequisite Workbook has been provided to assist in the development of the customized Prerequisite Program.

Step 4: 	Review the contents of the BAC Generic HACCP Plan with the food safety team.  Analyze your product descriptions and process flow steps from start (receiving) to finish (shipping) to identify hazards and how they are controlled, particularly those that are not covered by the Prerequisite Program.

Step 5:	Maintain all necessary records and written procedures.

Step 6:	Review the HACCP Plan when operational changes occur and on a regular basis (minimum annually) to ensure it reflects company standards and procedures.

HACCP Plan Document Control

Document Control Overview

The purpose of document control is to ensure that all documentation is properly updated, maintained, controlled, and the HACCP Plan remains up to date.

Many companies have already established ways of controlling documents.  When utilizing this Workbook, it is important to recognize how your company currently controls documents.  Depending on the extent to which this Workbook is used, you may choose to follow company specific document control measures or use those presented in this Workbook.

Document Revision

Changes are typically recorded on the Document Revision Log. This task is usually the responsibility of the HACCP Team Coordinator, as he/she usually possesses the ‘Master’ HACCP or Food Safety Manual.  The revision of documents occurs on an ongoing basis, as the need arises.

## Please see the BAC Prerequisite Programs Workbook, 
Section 2 on Document Control (FSM-002). Also, see the Appendix SOPs for a sample Document Control procedure.

Identify the document control activities that pertain to your operation and decide whether to incorporate all or some measures presented in the template.

How to use the BAC HACCP Workbook

Workbook Sections include:

- A purpose statement about the corresponding form.

- Instructions on how to complete each form relevant to the HACCP Plan.

- A blank copy of each form (so that the user may insert their company specific information (i.e. customize their HACCP Plan) while referring to the BAC Generic HACCP Plan.

Creating Your Own HACCP Plan

- Read the contents of the BAC Generic HACCP Plan.

- Read the instructions regarding how to complete each form.

- Answer the questions when filling out each provided blank form according to your internal processes and using the BAC Generic HACCP Plan as a guide.

- Ensure that the HACCP Team is involved in completing this Workbook.  Input, support, and understanding of each HACCP Team Member is essential in establishing this program and engaging the whole organization.

- Review the contents of the HACCP Plan on a regular basis (i.e. at least annually) and modify or update as required.

How To Document Your Own HACCP Plan

Option A – Use this Workbook to create a complete electronic template:

- make an electronic copy of this Workbook;

- complete the necessary sections;

- delete the ‘How to’ information and instructions; and

- customize using your company logo and document control procedures (deleting the BAC logo, etc.).

OR

Option B – Use this Workbook enhance an existing plan:

- copy the blank forms in this Workbook;

- complete the forms appropriately;

- customize the forms using your company’s document control practice; and

- insert into your company’s food safety plan.

HACCP Development Flow Chart

# FORM 1

# PRODUCT
DESCRIPTION

## How to complete Form 1

Purpose The purpose of Form 1 is to identify the important product characteristics, how the product is used, describe the packing and shelf life, where it will be sold, labelling, and special distribution control. This is done in order to identify specific food safety related concerns. The BAC Generic HACCP Plan identifies a single product (beer) and a description of the Brewing process.

Step 1: Complete a blank Form 1 for the product description (using the BAC Generic HACCP Plan - Form 1 as a guide.) A Generic template does not exist for product descriptions that are not listed in this Workbook (and the BAC Generic HACCP Plan). Ensure that the analysis is accurate with further education about HACCP or by consulting a HACCP expert for assistance.

Step 2: After you have completed the blank Form 1 provided below, proceed to Form 2.

## Blank 
Form 1

(See Next Page)

| Product Description : Beer Product Name: Beer |
| --- |
| 1. Product Name(s) |  |
| 2. Important Product Characteristics |  |
| 3. How it is to be used |  |
| 4. Packaging |  |
| 5. Shelf Life |  |
| 6. Where it will be sold |  |
| 7. Labelling instructions |  |
| 8. Special Distribution Control |  |

# FORM 2

# LIST OF
PRODUCT INGREDIENTS AND
INCOMING MATERIALS

## How to complete Form 2

Purpose The purpose of Form 2 is to list all the product ingredients and incoming materials (including raw materials, product ingredients, processing aids, and packaging materials) that are used or involved in producing beer. This is to identify all potential Biological (B), Chemical (C) and Physical (P) hazards that could apply to product ingredients and packaging materials.

Step 1: Identify the product ingredients that pertain to your operation: ‪Liquid Ingredients Potable Water City Water Well/ Surface Water Purchased Water Other: __________________ ‪Dry Ingredients Barley malt Wheat malt Hops Cereal grain e.g. wheat (non-malted), corn, oats, rice Other: ___________________ Primary Packaging Materials New and used glass Lined aluminum cans Lined aluminum bottles New and used stainless steel kegs Plastic bottles e.g. PET Crowns , Closures and Can Ends Other _________________ ‪Other Ingredients Caramel Dextrin

## How to complete Form 2 (Continued)

‪Other Ingredients (Continued) Food enzymes Amylase Glucoamylase Glucanase Papain Pentosanase Protease Other: ________________ Stabilizing agents Calcium Alginate Carrageenan Propylene Glycol Alginate Other: ________________ Water preparation agents Ammonium Phosphate Dibasic Calcium Chloride Calcium Hydroxide Calcium Sulphate Citric Acid Lactic Acid Magnesium Sulphate Phosphoric Acid Sulphuric Acid Other: ________________ Preservatives Ascorbic Acid Calcium Ascorbate Potassium Metabisulphite Sodium Metabisulphite Other: _________________ Yeast foods Manganese Sulphate Phosphoric Acid Zinc Sulphate Ammonium Persulphate (brewers’ yeast) Other: _________________

How to complete Form 2 (Continued)

‪Other Ingredients (Continued) Processing aids Irish Moss Seaweed Activated Carbon Magnesium Silicate Cellulose China Clay Diatomaceous Earth Gelatin Silica Gel Polyvinylpolypyrrolidone Wood Shavings derived from oak, beech, hazelnut or cherry wood; Dimethylpolysiloxane (wort) Hydrogen Peroxide (mash) Compressed Air Other: ___________________ Preservatives Ascorbic Acid Calcium Ascorbate Potassium Metabisulphite Sodium Metabisulphite Other: ___________________ Yeast Salt Hop oil Hop extract Liquid wheat extract Nitrogen Other: ___________________ Carbon dioxide Purchased CO2 Regenerated CO2 Other: ___________________ Carbohydrate matter Sucrose Syrup Honey Other: ___________________

How to complete Form 2 (Continued)

‪Primary Packaging Materials New and used glass Lined aluminum cans Lined aluminum bottles New and used stainless steel kegs Plastic bottles e.g. PET Crowns, Closures and Can Ends Other: _________________

Step 2: If you answered YES, include these product ingredient(s) and incoming material(s) when completing Form 2 (using the BAC Generic HACCP Plan: Form 2 as a guide). It may be beneficial to consult the purchasing department about product ingredients and incoming material listings. When listing the product ingredients and incoming materials, it is not necessary to include each size of a particular item, but it may be beneficial to indicate if the item is food grade. Ensure that the listing is representative of your operation (as opposed to merely listing all examples provided) and include any other information (e.g. if item is food grade) that may help identify potential hazards. If you answered NO, do not include these product ingredient(s) when completing Form 2. A generic template does not exist for ingredients or incoming materials not listed in this Workbook (and the BAC Generic HACCP Plan). Ingredients and incoming materials listed here are typical to the brewing process. However, individual brewery needs and new product innovations may result in the use of ingredients and materials that are not listed here. Those additional items need to be included in your plan.

Step 3: After you have completed the blank Form 2 provided, proceed to Form 3.

## Blank
Form 2

(See Next Page)

| List of Product Ingredients and Incoming Materials Product Name: Beer |
| --- |
| LIQUID INGREDIENTS | DRY INGREDIENTS (allowable) | PRIMARY PACKAGING MATERIALS |
| OTHER INGREDIENTS (allowable) | OTHER INGREDIENTS (allowable) | OTHER INGREDIENTS (allowable) |

# FORM 3

# PROCESS FLOW
DIAGRAM

# How to complete Form 3

Purpose The purpose of Form 3 is to draw a diagram of how product ingredients and materials flow through your operation (from receiving to shipping). This analysis will assist in identifying where potential hazards could be introduced during the flow of product and incoming materials. A process flow diagram can be constructed with interviews, observations of operations, and other sources of information such as blueprints. There has to be enough detail to be useful in hazard identification, however, not so much as to overburden the plan with less important points.

Step 1: Identify what steps represent the product and material that are transported, received, handled, and shipped by your operation. When developing any of the process flow diagrams, ensure to have the BAC Generic HACCP Plan as a direct reference to reconstruct the process flow diagrams that reflect your operation. Process Flow Diagram: Beer Making Process Overview Step ID Description Y/N PS1 Receiving PS2 Storage & Handling PS3 Brewing - - Milling - Mashing - Lautering - Kettle - Whirlpool - Cooling PS4 Fermentation PS5 Aging - Clarification - Filtration PS6 Bright Beer Storage PS7 Bright Beer Processing PS8 Packaging PS9 Warehousing/Shipping

# How to complete Form 3 (Continued)

Process Flow Diagram: PS3 - BREWING ‪Step ID Description Y/N B1 Receiving (See PS1) B2 Storage (See PS2) B3 Milling B4 Cereal Cooker B5 Mashing (Mash Mixer, Mash Cooker) B6 Lautering (Lauter Tun, Mash Filter r moval of spent grains B7 Holding Tank B8 Kettle B9 Whirlpool/ Centrifuge/ Hot Wort Tank B10 Wort Cooling (Heat Exchanger)

# How to complete Form 3 (Continued)

Process Flow Diagram: PS4 - FERMENTATION ‪Step ID Description Y/N F1 Wort O ygenati n/ Wort Aeration F2 Fermentation F3 Cooling F4 G een Beer Process Flow Diagram: PS4 - FERMENTATION SUB-PROCESS - YEAST PREPARATION ‪Step ID Description Y/N Y1 Propagation Y2 Storage Y3 Acid Washing Process Flow Diagram: PS5 - AGING/ CLARIFICATION / FILTRATION ‪ Step ID Description Y/N 1 Cooling A2 Buffer Tank A3 Centrifuge A4 Buffer tank A5 Cooling A6 Aging Tank A7 Secondary Storage A8 Surge/ buffer Tank A9 DE Pre-filter/ Filter Trap/ Sheet Filter Membrane ilter/ PVPP Filter A10 Bright Beer Storage

# How to complete Form 3 (Continued)

Process Flow Diagram: PS7 BRIGHT BEER PROCESSING A – Sterile Filtration Step ID Description Y/N SF1 Bright Beer Tank SF2 Sterile Filtration SF3 Sterile Beer Tank Process Flow Diagram: PS7 BRIGHT BEER PROCESSING B – Flash Pasteurization ‪ Step ID Description Y/N FP1 Flash pasteurization FP2 Pasteurized Beer Tank Process Flow Diagram: PACKAGING PROCESSES (PS8) PS8 RB – Returned Bottles Prep (Float Glassware Prep) ‪ Step ID Description Y/N RB1 Receivin / Storage RB2 De-palletizing RB3 De-casing RB4 Human (Visual) Inspection RB5 Bottle Wash Loading RB6 Pre-rinse sprays RB7 Soak Tanks With Caustic RB8 Hydro Jet Sprays RB9 Post-Soak RB10 External Flush RB11 External and internal Rinse RB12 Interior Final Rinse RB13 External Final Rinse

# How to complete Form 3 (Continued)

Process Flow Diagram: New Bottles (Glassware) Prep Step ID Description Y/N NB1 Receiving NB2 Preliminary Inspection NB3 Storage NB4 Collect the Manufacturing Pallet tags NB5 Pallet prep NB6 De-palletize NB7 Visual Inspection NB8 Bottle Loading NB9 Bulk Glass Rinser

# How to complete Form 3 (Continued)

Process Flow Diagram: PACKAGING PROCESSES PS8 BT - BOTTLING ‪ Step ID Description Y/N BT1 Empty Bottle Inspection BT2 Down bottle filler in-feed control BT3 Purges & Evacuation & Positive Pressure BT4 Filling BT5 Fobbing BT6 Crowning BT7 Crowner Flush (external) BT8 Filled Bottle wash external BT9 Pasteurize BT10 Foam Inspection/ Candling Inspection BT11 Bottle Drying and Air Knives BT12 Labelling BT13 Primary Packaging, Coding BT14 Filled Bottle Inspection BT14 Filled Bottle Inspection BT15 Divert to packers BT16 Carton Forming BT17 Case Packing BT18 Case Sealing BT19 Secondary Packaging Code BT20 Full Case Inspection BT21 Palletize BT22 Storage (or Live Load) BT23 Shipping

# How to complete Form 3 (Continued)

Process Flow Diagram: PACKAGING PROCESSES PS8 (K) - KEGGING ‪ Step ID Descr ption Y/N K1 Receiving (See PS1) K2 Storage & Handling (See PS2) K3 De-palletizing (See PS2) K4 External Inspection K5 Ext Wash K6 Post Wash Inspection K7 Racking K8 Purge to Empty K9 Flush K10 Wash K11 Purge to empty K12 Rinse K13 Sterilize & Hold K14 Purge to Empty K15 Counter Pressure K16 Barnes Neck Sanitize K17 Inspect K18 Filling K19 Sterilize Barnes Neck K20 Final Rinse Dome K21 Chemical Sanitize Barnes Neck K22 Dust Cap K23 Air Dry K24 Product Code Applied K25 In-line weighing K26 Palletize K27 Storage or Live Load K28 Shipping

# How to complete Form 3 (Continued)

Process Flow Diagram: PACKAGING PROCESSES PS8 (C) - CANNING ‪ Step ID Description Y/N C1 Receiving C2 Storage & Handling C3 Collect & Timestamp Can Pallet ID C4 De-palletize to mass conveyor C5 Online visual inspection C6 Primary code applied C7 Bulk in-line rinser C8 Filling (pre-evacuation & beer fill) C9 Bubble breakers C10 Under Cover Gassing C11 Collect manufacturing lot detail for ends C12 Double seaming C13 Filler valve monitor C14 External Can Flush C15 Pasteurizer C16 Pre-Blower Station C17 Final Dryer Station C18 Fill Height Inspection C19 Divert to Packers C20 Hi-Cone Machine C21 Case Packers C22 Visual Inspection C23 Tray Machine C24 Secondary Code applied C25 Transfer to Palletizer C26 Storage (or Live Load) C27 Shipping

# How to complete Form 3 (Continued)

Process Flow Diagram: PS8 T - TANKERING ‪Step I Description Y/N T1 Empty Tanker T2 Tanker Washing T3 Tanker Purging T4 Tanker Filling T5 Tanker Shipping T6 Full Tanker Receiving T7 Full Tanker Unloading

Step 2: If you answered YES, include these steps when completing Form 3 (using the BAC Generic HACCP Plan: Form 3 as a guide). If you answered NO, do not include these steps when completing Form 3. A Generic template does not exist for steps not listed in this Workbook (and the BAC Generic HACCP Plan). Ensure that the analysis is accurate with further education about HACCP or by consulting a HACCP expert for assistance.

Step 3: After you have completed the blank Form 3 provided, proceed to Form 4.

## Blank
Form 3

(See Next Page)

Beer Making Process

# Form 4

# PLANT LAYOUT WITH EMPLOYEE / PRODUCT FLOW

## How to complete Form 4

Purpose The purpose of Form 4 is to show product flow and employee traffic patterns within the plant. The diagram should include the flow of all ingredients and packaging materials from the moment they are received at the plant, through storage, preparation, processing, holding, and shipping. The personnel flow should indicate employee movement through the plant, including change rooms, washrooms and lunchrooms. The location of hand wash facilities and footbaths (if applicable) should also be noted. This plan should aid in the identification of any areas of potential cross contamination within the establishment. Once the process flow diagrams and plant layout have been drafted, they must be verified by an on-site inspection for accuracy and completeness. This will ensure that all the major process steps have been identified. It will also validate the assumptions made with respect to the movement of product and employees in the facility.

Step 1: Do you have a diagram of your operation that indicates how and where products and employees flow? ‪YES ‪ NO If you answered YES, provide your plant layout diagram that shows product and employee flow here. If you answered NO, develop a plant layout diagram (showing product and employee flow) on the blank Form 4 provided or by any other means (e.g. electronic version). The plant layout diagram does not have to be a complete blueprint of the operation, or to be done by a professional, but it does have to represent the plant and to be verified by an actual comparison of what is occuring on the plant floor. It has to be comprehesive enough for anyone to understand the flow of products and employees. (Note: Due to the size and complexity of your operation, the blank Form 4 provided may not be of adequate size.)

Step 2: After you have completed the blank Form 4 provided, proceed to Form 5.

## Example of Form 4

Plant Specific Product Flow Diagram & Employee Traffic Pattern Diagram

on next page

Schematic Diagram

Legend

Employee Flow:

Product Flow:

# Form 5

# Biological Hazard Identification

# How to complete Form 5

Purpose Form 5 identifies the biological hazards that are associated with the product ingredients and materials used in a brewery. It also identifies where and how the biological hazards could be controlled. Analysis of the ingredients (listed on Form 2 of the BAC Generic HACCP Plan) and the process steps (listed on Form 3 of the BAC Generic HACCP Plan) has been completed on Form 5 of the BAC Generic HACCP Plan.

Step 1: Compare the product ingredients and incoming materials on your brewery’s Form 2 and the process flow steps on your brewery’s Form 3 to those identified in the BAC Generic HACCP Plan. With the HACCP team, conduct a hazard analysis (using the Generic HACCP plan as a guide). Using your completed Forms 2 and 3, complete Form 5.

Step 2: Transfer the identified product ingredients and incoming materials and process flow steps as well as their corresponding hazard analysis to the blank Form 5 provided. The “controlled at” is not completed at this time. The “controlled at” column is to be completed on Form 5A after Form 8 has been completed (Note: Due to the size and complexity of your operation, the blank Form 5 provided may not be of adequate size.)

Step 3: After you have completed the blank Form 5 provided, proceed to Form 6.

## Blank
Form 5

(See Next Page)

| Biological Hazard Identification |
| --- |
| Ingredients | Biological Hazard Identification | Controlled at (i.e. Prerequisite Program, SOP, GMP, Form 9 or CCP) |
|  |  | Note: This column is to be completed on Form 5a, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 5a, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 5a, after Form 8 is completed. |
| Processing Steps | Biological Hazard Identification | Controlled at (i.e. Prerequisite Program, SOP, GMP, Form 9 or CCP) |
|  |  | Note: This column is to be completed on Form 5a, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 5a, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 5a, after Form 8 is completed. |

# FORM 6

# CHEMICAL HAZARD IDENTIFICATION

# How to complete Form 6

Purpose Form 6 identifies the chemical hazards that are associated with the product ingredients and materials used in a brewery. It also identifies where and how the chemical hazards could be controlled. The analysis for the ingredients (listed on the Form 2 of the BAC Generic HACCP Plan) and the process steps (listed on Form 3 of the BAC Generic HACCP Plan) has been completed on Form 6 of the BAC Generic HACCP Plan.

Step 1: Compare the product ingredients and incoming materials on your brewery’s Form 2 and the process flow steps on your brewery’s Form 3 to the hazard analysis that has been completed for Form 6 of the BAC Generic HACCP Plan. With the HACCP team, conduct a hazard analysis (using the Generic HACCP plan as a guide). Using your completed Forms 2 and 3, complete Form 6.

Step 2: Transfer the identified product ingredients and incoming materials and process flow steps as well as their corresponding hazard analysis to the blank Form 6 provided. The “controlled at” is not completed at this time. The “controlled at” column is to be completed on Form 6A after Form 8 has been completed. (Note: Due to the size and complexity of your operation, the blank Form 6 provided may not be of adequate size.)

Step 3: After you have completed the blank Form 6 provided, proceed to Form 7.

## Blank
Form 6

(See Next Page)

| Chemical Hazard Identification |
| --- |
| Ingredients | Chemical Hazard Identification | Controlled at (i.e. Prerequisite Program, SOP, GMP, Form 9 or CCP) |
|  |  | Note: This column is to be completed on Form 6A, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 6A, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 6A, after Form 8 is completed. |
| Processing Steps | Chemical Hazard Identification | Controlled at (i.e. Prerequisite Program, SOP, GMP, Form 9 or CCP) |
|  |  | Note: This column is to be completed on Form 6A, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 6A, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 6A, after Form 8 is completed. |

# Form 7

# PHYSICAL HAZARD IDENTIFICATION

## How to complete Form 7

Purpose Form 7 identifies the physical hazards that are associated with the product ingredients and materials used in a brewery. It also identifies where and how the physical hazards could be controlled. The analysis for the ingredients (listed on the Form 2 of the BAC Generic HACCP Plan) and the process steps (listed on Form 3 of the BAC Generic HACCP Plan) has been completed on Form 7 of the BAC Generic HACCP Plan.

Step 1: Compare the product ingredients and incoming materials on your brewery’s Form 2 and the process flow steps on your brewery’s Form 3 to the hazard analysis that has been completed for Form 7 of the BAC Generic HACCP Plan. With the HACCP team, conduct a hazard analysis (using the Generic HACCP plan as a guide). Using the your completed Forms 2 and 3, complete Form 7.

Step 2: Transfer the identified product ingredients and incoming materials and process flow steps as well as their corresponding hazard analysis to the blank Form 7 provided. The “controlled at” is not completed at this time. The “controlled at” column is to be completed on Form 7A after Form 8 has been completed. (Note: Due to the size and complexity of your operation, the blank Form 7 provided may not be of adequate size.)

Step 3: After you have completed the blank Form 7 provided, proceed to Form 8.

## Blank
Form 7

(See Next Page)

| Physical Hazard Identification |
| --- |
| Ingredients | Physical Hazard Identification | Controlled at (i.e. Prerequisite Program, SOP, GMP, Form 9 or CCP) |
|  |  | Note: This column is to be completed on Form 7A, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 7A, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 7A, after Form 8 is completed. |
| Processing Steps | Physical Hazard Identification | Controlled at (i.e. Prerequisite Program, SOP, GMP, Form 9 or CCP) |
|  |  | Note: This column is to be completed on Form 7A, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 7A, after Form 8 is completed. |
|  |  | Note: This column is to be completed on Form 7A, after Form 8 is completed. |

# Form 8

# CRITICAL CONTROL POINT IDENTIFICATION

## How to complete Form 8

Purpose Form 8 analyzes the biological, physical, and chemical hazards that are identified in Forms 5, 6, and 7. The hazards are analyzed by answering the questions of the Decision Tree (Q1 to Q4) in Form 8. This process (Q1 to Q4) will identify if any of the hazards is a Critical Control Point (CCP). If the analysis identifies a CCP (No to Q4), monitoring and verification must be applied for a complete HACCP Program.

Step 1: Identify the product ingredients and incoming materials and the process flow steps hazard analysis (on Forms 5, 6, and 7 that you completed above) that has been completed for Form 8 of the BAC Generic HACCP Plan.

Step 2: Transfer the identified product ingredients and incoming materials and process flows steps hazard analysis on to the blank Form 8 provided. Proceed to question one only if you have answered NO to the prescreening question that asks if the hazard is fully controlled by a Prerequisite Program. With the HACCP Team, ensure that the answers to the Decision Tree questions (Q1 to Q4) correspond to your operation. Use the legend as in the BAC Generic HACCP Plan: Q = Is this hazard fully controlled by prerequisite program(s)? Which prerequisite program(s)? Example: Hazard of Coliform & E.Coli for City Water is fully contolled in the Prerequisite program for Premises, water quality section 4.1. In this column enter PP- Premises, Water Quality (A.4.1) Q1 = Could a control measure(s) be used by the operator at any process step? Q2 = Is it likely that contamination by the identified hazard could occur in excess of the acceptable level or could increase to an unacceptable level? Q3 = Is this process step specifically designed to eliminate or reduce the likely occurrence of the identified hazard to an acceptable level? Q4 = Will a subsequent step eliminate the identified hazard or reduce its likely occurrence to an acceptable level?

Step 3: After you have completed the blank Form 8 provided, proceed to Form 3A.

Step 4: The completed Form 5, Form 6 and Form 7 are copied to create Form 5a, Form 6a and Form 7a. The “controlled at” column is to be completed on Form 5A, Form 6A and Form 7A after Form 8 has been completed, using the information on Form 8. Information from Form 8 is also used to complete Form 9 and Form 10.

## Blank
Form 8

(See Next Page)

| Incoming material/ process step/ hazards on schematic diagram | Category and identified hazard. | Determine if fully controlled by prerequisite program. *If “yes” = indicate “Prerequisite Program” and proceed to next identified hazard. *If “no” = proceed to question1 (Q1). | Q1. Could a control measure(s) be used by the operator at any process step? If NO = not a CCP + identification on how this hazard will be controlled before and after the process + proceed to the next identified hazard If YES = description + next question (Q2) | Q2. Is it likely that contamination with the identified hazard could occur in excess of the acceptable level or could increase to an unacceptable level? If NO = not a CCP + proceed to the next identified hazard If YES = next question (Q3) | Q3. Is this process step specifically designed to eliminate/reduce the likely occurrence of the identified hazard to an acceptable level? If NO = next question (Q4) If YES = CCP + go to last column | Q4. Will a subsequent step eliminate the identified hazard or reduce likely occurrence to an acceptable level? If NO = CCP + go to last column If YES = not a CCP + identify subsequent step + proceed to the next identified hazard | CCP Number + proceed to next identified hazard |
| --- | --- | --- | --- | --- | --- | --- | --- |

Date: _____________________ Approved by: ___________________________________________________________

# Form 3A

# PROCESS FLOW DIAGRAM WITH CCPS

## How to complete Form 3A

Purpose The purpose of Form 3A is to identify the critical control points in the process flow diagram.

Step 1: Transfer all process flow diagrams from Form 3 to Form 3A.

Step 2: Add the CCP code (e.g. CCP3-P) directly into the process flow boxes that were designated as CCPs in Form 8.

Step 3: After you have completed Form 3A, proceed to Form 5A.

## Blank
Form 3A

(See Next Page)

Brewing Process

# Form 5A

# BIOLOGICAL
HAZARD IDENTIFICATION AND CONTROL

## How to complete Form 5A

Purpose Form 5A is an extension of Form 5 in that the “controlled at” measure cannot be determined until the Hazard Analysis on Form 8 is completed.

Step 1: Transfer the contents of Form 5 that you completed above. Rename Form 5 to Form 5A. Complete the “controlled at” column by transferring the controls identified in Form 8. With the HACCP Team, ensure that this column is reflective of what occurs in your operation. Use the prerequisite references as in the BAC Generic HACCP Plan: For Example: Hazard of Coliform & E.Coli for City Water is controlled in the Prerequisite program for Premises, water quality section 4.1. Under the “Controlled at” column enter PP- Premises, Water Quality (A.4.1)

Step 2: Add the letter ‘B’ (for Biological) beside the relevant product ingredient(s) on Form 2 and in the relevant process step box in Form 3.

Step 3: After you have completed the blank Form 5A provided, proceed to Form 6A.

## Blank
Form 5A

(See Next Page)

| Biological Hazard Identification |
| --- |
| Ingredients | Biological Hazard Identification | Controlled at |
| Processing Steps | Biological Hazard Identification | Controlled at |

# Form 6A

# Chemical Hazard
Identification and Control

## How to complete Form 6A

Purpose Form 6A is an extension of Form 6 in that the “controlled at” measure cannot be determined until the Hazard Analysis on Form 8 is completed.

Step 1: Transfer the contents of Form 6 that you completed above. Rename Form 6 to Form 6A. Complete the “controlled at” column by transferring the controls identified in form 8. With the HACCP Team, ensure that this column is reflective of what occurs in your operation. Use the prerequisite references as in the BAC Generic HACCP Plan: For Example: Hazard of contamination from coolant for FP2 Pasteurization is controlled in the Prerequisite program for Equipment section 1.2. Under the “Controlled at” column enter PP- Equipment( C.1.2).

Step 2: Add the letter ‘C’ (for Chemical) beside the relevant product ingredient(s) on Form 2 and in the relevant process step box in Form 3. If the letter B has already been added, place the C beside it.

Step 3: After you have completed the blank Form 6A provided, proceed to Form 7A.

## Blank Form
6A

(See Next Page)

| Chemical Hazard Identification |
| --- |
| Ingredients | Chemical Hazard Identification | Controlled at |
| Processing Steps | Chemical Hazard Identification | Controlled at |

# Form 7A

# Physical Hazard
Identification and Control

## How to complete Form 7A

Purpose Form 7A is an extension of Form 7 in that the “controlled at” measure cannot be determined until the Hazard Analysis on Form 8 is completed.

Step 1: Transfer the contents of Form 7 that you completed above. Rename Form 7 to Form 7A. Complete the “controlled at” column by transferring the controls identified in form 8. With the HACCP Team, ensure that this column is reflective of what occurs in your operation. Use the prerequisite references as in the BAC Generic HACCP Plan: For Example: Hazard of Glass or Metal for Wheat is controlled in the Prerequisite program for Transportation Receiving & Storage section 1.1. Under the “Controlled at” column enter PP- Transportation Receiving & Storage (B.1.1)

Step 2: Add the letter ‘P’ (for Physical) beside the relevant product ingredient(s) on Form 2 (e.g. Spout P) and in the relevant process step box in Form 3. If the letters B or C have already been added, place the P beside it.

Step 3: After you have completed the blank Form 7A provided, proceed to Form 9.

## Blank Form
7A

(See Next Page)

| Physical Hazard Identification |
| --- |
| Ingredients | Physical Hazard Identification | Controlled at |
| Processing Steps | Physical Hazard Identification | Controlled at |

# Form 9

# HAZARDS NOT CONTROLLED BY OPERATOR

## How to complete Form 9

Purpose Form 9 identifies the ingredients and materials and process flow steps are not in the control of your operation, but in the control of the supplier and/or manufacturer and/or producer and/or customer. This will identify other responsibility of control of the food safety hazards.

Step 1: Identify the product ingredient(s) and material(s) and the process flow step(s) (on Form 8 that you completed above) on Form 9 of the BAC Generic HACCP Plan.

Step 2: Transfer the identified product ingredients and materials and processing steps that are not controlled by your facility (the “operator”) on to the blank Form 9 provided. (Note: Due to the size and complexity of your operation, the blank Form 9 provided may not be of adequate size.)

Step 3: After you have completed the blank Form 9 provided, proceed to Form 10.

## Blank Form
9

(See Next Page)

| Form 9 – Hazards Not Controlled by Operator |
| --- |
| Ingredients/Processing Step | Biological Hazard = B Chemical Hazard = C Physical Hazard = P | Operator does not control hazard. Indicate the way the hazard could be addressed: |

# Form 10

# HACCP Plan

## How to complete Form 10

Purpose Form 10 identifies the critical control points (CCPs) and where a CCP occurs as well as its cause and result. Form 10 also includes critical limits, monitoring procedures, deviation procedures, verification procedures, and HACCP records, logs or documentation. This ensures that CCPs are handled consistently, can be verified, and are under control, which will minimize the occurrence of food safety issues.

Step 1: Identify the CCP on Form 10 of the BAC Generic HACCP Plan and compare to the analysis completed on Form 8 above.

Step 2: Transfer the identified CCP and its corresponding information from Form 10 of the BAC Generic HACCP Plan to the blank Form 10 provided. With the HACCP Team, ensure that the CCP identification and its accompanying information (critical limits, monitoring procedures, deviations and corrective actions, and verification activities) correspond to your operation. Review background information at least on an annual basis. (Note: Due to the size and complexity of your operation, the blank Form 10 provided may not be of adequate size.)

Components of Form 10

Explanation/Definition of Form 10 Components Process Steps Identified process step and associated step number (example Empty Bottle Inspection – EBI Step BT1) CCP/Hazard Number (CCP#) A CCP is any point, step or procedure in a specific food system where loss of control may result in an unacceptable health risk. A number is given to every identified CCP and a letter (B, C, or P) to identify the hazard type. (e.g. the first CCP in the process would be named CCP 1. If it controlled a physical hazard it would be named CCP 1-P). Hazard Description Identify hazard(s) that could occur if the CCP is not controlled, monitored, and verified. Identify the potential hazards at all stages of the operation (receiving, manufacture, and distribution, until the point of consumption - Any microbiological, chemical or physical property that may cause an unacceptable consumer health risk). Critical Limits Target levels and tolerances, which must be met to ensure that the CCP is under control. (These usually include: time, temperature, weight/size, humidity, water activity, pH, acidity, preservatives, salt level, and viscosity.) Monitoring Procedures A monitoring system to ensure control of the CCP by scheduling, testing or observations. (Methods of monitoring CCPs include: measurement of pH, time, temperature, or water activity and observation of employee activities and processes.) Deviation Procedures Corrective actions that are taken when there is a deviation identified by monitoring of a CCP. Four activities in a corrective action or deviation procedure include: (1) the use of monitoring to adjust the process to maintain control, (2) if control is lost, non-compliant issue is rectified, (3) correct the cause of noncompliance, and (4) maintain records of the corrective action Verification Procedures Implemented procedures to verify that the HACCP system is working correctly. Verification includes application of: methods, procedures, tests (samples), and other evaluations in addition to monitoring. HACCP Records Documentation concerning all procedures and records appropriate to HACCP principles and their application.

## Blank Form
10

(See Next Page)

| HACCP PLAN FORM #10 PRODUCT NAME: |
| --- |
| Process Steps | CCP/Hazard Number | Hazard Description | Critical Limits | Monitoring procedures | Deviation Procedures | Verification Procedures | HACCP Records |

END of WORKBOOK

Congratulations!

# Text boxes

Form 1 (Identify product descriptions)

Form 5 (Biological hazard identification of product ingredients and process flow) Note: no control measures stated

Form 2 (List of ingredients and incoming materials)

Form 3 (Process flow diagram – from receiving to shipping)

Form 6 (Chemical hazard identification of product ingredients and process flow) Note: no control measures stated

Form 7 (Physical hazard identification of product ingredients and process flow) Note: no control measures stated

Form 8 (Hazard analysis and Critical Control Point (CCP) determination or product descriptions and process flow)

Form 5A (Biological hazard identification of product ingredients and process flow) Note: control measures stated

Form 6A (Chemical hazard identification of product ingredients and process flow) Note: control measures stated

Form 7A (Physical hazard identification of product ingredients and process flow) Note: control measures stated

Form 9 (Hazards not in control of the operator)

Form 10 (HACCP Plan – CCP details)

Form 3A (Process flow diagram – from receiving to shipping) Note: CCPs stated

Garbage

Recycling

Shipping Door

Handwash sink

Office/Admin/Lab

Packaging/Palletizing

Chemical Storage

Process Work Area

Product Storage

Process Work Area

STORAGE

Process Work Area

Handwash sink

Receiving Door

Employee Entrance